## Slide 1: Exercise 27: AVA Analysis
AVA Analysis Barracouta
Your Task:
  Use some information from a seismic gather to predict hydrocarbon fill levels (gas cap, oil leg, water leg) within a reservoir on a seismic line.
Notes: A review of this exercise (Exercise 27).

## Slide 2: Amplitude vs Angle for the Gather
0 4 8 12 16 20 24 28 32 36
-20
-40
-60
-80
-100
-120
0
Intercept = ________
Slope = ________
-7
-3.5
DEGREE | AMPLITUDE
4 | -20
8 | -35
12 | -49
16 | -65
20 | -79
24 | -94
28 | -109
32 | -123
36 | -138
-140
Notes: My plot of the angle (degree) and amplitude pairs and straight line fit. I come up with an intercept of -7. I come up with a slope of -3.5.

## Slide 3: Modeled AVA Response
4
8
Intercept
Slope
0
-4
-8
0
-10
10
-20
Shale Baseline
Brine
Oil
Gas
Notes: When I plot my intercept, slope point on this diagram, it falls in the oil “cloud.” Thus, I predict the reservoir has oil in the pore space at the location of the gather.
NOTE: This is fictitious – the actual field does not have as thick of an oil leg as this exercise indicates.

## Slide 4: AVA-Based Fluid Classification
Gather
Possible
Fluid
Contact
Top of
Reservoir
Notes: Here the (fictitious) AVA responses have been plotted for the top of the reservoir. This is Figure 5 from the exercise.

## Slide 5: Predicted HC Distribution
Gather
Top of
Reservoir
Possible
Fluid
Contact
Notes: Here is the interpreted reservoir fluid distribution within the anticline – based on my fictitious AVA data.

## Slide 6: Exercise 27
Questions?