## Slide 1: Petroleum Geology & Geophysics
Time-Depth Conversion
V = 2800 m/s
Target
Apparent Time Structure
V = 5000 m/s
Sand / Shale
Limestone
Target
True Depth Structure
Notes: Slide 28.1 Title slide with some images

## Slide 2: Objectives
Understand the importance of time-depth conversion
Review velocity basics
Choosing a time-depth conversion method
Applying Corrections
Notes: Four (4) main objectives of this lecture.

## Slide 3: When is Time-Depth Important?
(after D. Marsden, 1993)
In all phases of Exploration, Development & Production
Logs , Cores
VSPs , Check shots
Seismic
Processing
Rock/Fluid
Prediction
Mapping in Depth
Post Well
Appraisal
Seismic
Survey
Planning
Well Placement
And Drilling
Seismic
Acquisition
Velocity
is the Key
Vp and Vs (x,y,z)
Notes: Velocity data provide the relationship between travel times in seconds, our basic seismic measurement, to depth in feet or meters. Seismic data are in vertical units of two way travel time, so V= depth * TWT/0.5, or Depth = V * TWT/2.
In exploration, there is little or no well control. The most important use of time-depth conversion is to validate structural interpretations. A good depth conversion can make time structural highs appear or disappear. In development, there may be enough well control to define the reservoir, so the most important uses of depth conversion arises from the need to more accurately assess volumetrics (gross thickness, spill point identification etc.) and perform economic calculations.
The depth conversion is for well planning and geologic modeling in use for production purposes, the main focus of time. High angle wells are commonly used to minimize drilling costs while often trying to penetrate small target intervals. Geologic models are often built in depth so it is important that the particular velocity model a geologic modeler uses ties to all the well control.

## Slide 4: Time Interpretation Pitfalls
Scenario 1: Lithologies with anomalously high velocities can produce structural pull-up in the time domain. Proper depth conversion will remove false structures.
Sand / Shale
Limestone
Target
True Depth Structure
V = 2800 m/s
Target
Apparent Time Structure
V = 5000 m/s
Notes: When there is an anomalously high or low velocity interval that changes thickness laterally, the shapes that we see on a TWT seismic section can be significantly distorted.
On this slide, we have a high-velocity limestone that varies in thickness. On the left, the base of the limestone is flat in true depth. However, on the time section on the right, the base of the limestone is NOT flat; the base has been “pulled up” in time. All deeper layers would also have a false pull-up that might be mis-interpreted as structural highs worth drilling.

## Slide 5: Time Interpretation Pitfalls
Shale
Gas Sand
True Depth Structure
Target
Apparent Time Structure
V = 3000 m/s
Target
Scenario 2: Lithologies with anomalously low velocities can produce structural sags in the time domain. Proper depth conversion may reveal true structures that are masked on time data.
V = 2000 m/s
Notes: On this slide, we have a low-velocity gas sand lens – the thickness varies laterally. On the left, the top of the target has a high in true depth. However, on the time section on the right, the top of the target appears to be a low; this horizon has been “pushed down” in time. All deeper layers would also have a false push-down. For this example, working on TWT section would “hide” a potential structural high that might be worth drilling.

## Slide 6: Time Interpretation Pitfalls
rugose water bottom
dipping water bottom
flat water bottom
Scenario 3: Steeply dipping or rugose water bottom may cause pull up or push down on two-way time seismic data
Depth
Depth
Depth
Rugose Water Bottom
Dipping Water Bottom
Flat Water Bottom
Complex
Simple
Notes: In areas where the water bottom is not nearly horizontal, we can also have distortions of true shapes on time sections. Here we show three (3) depth sections. The deep anticline is the same on all three, but the water bottom has different shapes. The next slide shows the TWT representation for these three (3) depth sections.

## Slide 7: Time Interpretation Pitfalls
Time
Time
Time
Methodology should plan for water effects
Complex
Simple
rugose water bottom
dipping water bottom
flat water bottom
Scenario 3: Steeply dipping or rugose water bottom may cause pull up or push down on two-way time seismic data
Notes: Where the water bottom is nearly flat (left), the deep anticline has the correct shape. The dipping water bottom (center) has pulled-up the left flank of the anticline and pushed=down the right flank. Not only is the shape of the anticline incorrect, the location of the highest point (crest of anticline) may appear to be in the wrong location. On the right, oscillations in the water bottom has superimposed oscillations on the horizon at the top of the anticline.

## Slide 8: Geologic Controls on Velocity
AGE
Burial History (compaction state)
Structural History
(uplift and erosion)
Depth
Temperature gradient
Pressure Gradient
Abnormal Pressure
Lithology
  Depositional environment
  Grain size
  Porosity
  Fluid content
  Total organic content
  Maturation
Notes: Geology controls the velocities in the earth. These are some of the major controlling factors on velocity. Overall, velocities increase with depth as rocks get deeper, more compacted, older, hotter and under more pressure. However, in most cases an assumption of a single function for how velocity increases with depth is a poor model of the real earth. The more you know about the geological controls on the velocities in your study area, the better you can plan and execute a depth conversion.

## Slide 9: Sources of Velocity Information
1) Well Based Velocities
  Sonic Logs
  Check shots or VSP surveys
  Pseudo Velocities – from well tops and seismic times
2) Seismic Based Velocities
  Stacking velocities – Vavg and Vint from Dix equation
  Tomography – travel time inversion using horizons & stacking velocities
Notes: We have two (2) main sources for information on the local velocity structure. If we have wells that have had sonic logs run in them, that is a primary source for good velocity information. We can get more accurate velocity information from check shot surveys or VSPs, if available for some of the wells. If we have a good well-seismic tie by means of a synthetic trace, then we can get pseudo-velocities by linking well tops to seismic times.
Our other source of velocity data is from seismic processing. We get estimates of velocity as a function of depth when we stack multi-fold seismic data. Stacking velocities can give us either average velocities on interval velocities using the Dix equation. Stacking velocities are not highly accurate, so you must remember they are only a first-order estimate. If the seismic processing includes tomography, very expensive in terms of money, time and people, then the velocity data is fairly accurate. Very few seismic data sets have this high-end processing available.

## Slide 10: Velocity Definitions
Interval Velocity
Interval thickness divided by interval time
Determined from well logs and check shot data
Average Velocity
Depth to a point divided by time to that point
From check shot data or integrated sonic
RMS Velocity
Root mean square average of interval velocities, which
assumes a flat, homogeneous layered earth
From check shot data or integrated sonic
Vnmo Velocity
Normal moveout velocity or stacking velocity, which
is an empirical value used to flatten events on
velocity gathers
Dix Interval Velocity
Interval thickness derived from the Dix equation
See slide 12
Well Based
Seismic
Based
Notes: This slide gives definitions for five (5) types of velocity. The first three (3) are velocities derived from well data; the last two (2) are seismically derived. Slides 11 and 12 help explain these.

## Slide 11: Typical Time-Depth Curve
Two-Way Time, T
Depth, Z
Vavg = Z/(T/2)
Vint = ΔZ/(ΔT/2)
Notes: Here we have five (5) depth-TWT pairs derived from either well or seismic data. Average velocity (blue) is the total depth to a point on the curve divided by the total one-way time to that point. Average velocity tends to smear all the geology above the point down to which it is calculated.
Interval velocity (green) is calculated between two (2) consecutive points. It is the change in depth between the two (2) points divided by the change in one-way time. Interval velocity gives information about the geology between the two depth points (top and base of interval).

## Slide 12: Dix Interval Velocity
Dix Interval Velocity
Interval velocities are derived from the Dix equation
We assume that Vnmo is equal to Vrms
Thus, we substitute Vnmo, which we get from seismic
processing, for Vrms
Vdixn =
(Vrms,n2 * Tn) – (Vrms,n-12 * Tn-1)
Tn – Tn-1
Notes: This slide gives the equation for the Dix equation. It also has the basic assumption that Vnmo is equal to Vrms.

## Slide 13: For Depth Conversion
If we have sonic logs from wells, ideally with check shots, then we can derive:
          VINT
          VAVG
If we have to use seismic data alone, we use the Dix equation to calculate VINT by assuming VNMO ~ VRMS
VNMO ~ VRMS when:
        Reflectors are planar and non-dipping
        No lateral velocity changes exist
        Shot-to-geophone offset is small compared to the depth of the reflector
Notes:           Well data might provide us with sonic logs and check shot data that would give us VINT, VAVG, and VRMS at the well locations. Seismic velocities are acquired by offset shots and receivers. They provide only first-order approximations. If we assume that VNMO ~ VRMS, then we can use the Dix equation to get interval velocities.

## Slide 14: Choosing a Time-Depth Method
For my study area, which
Time-Depth Conversion Method should I use?
?
Notes: There are several methods to perform a time-depth conversion. Some are fast and inexpensive, but may not be very accurate. Other methods are quite accurate, but are costly in terms of money, time, and people. Thus, a critical question is “For my study area, which time-depth conversion method should I use?”

## Slide 15: Time to Depth Methods
  The objective of the exploration problem
  The nature of the subsurface
  The complexity of the velocity structure
  The type of velocity data available
  The time available to do the conversion
  The budget available
The choice of a time/depth conversion method for a particular area depends on several factors:
  A reliable depth conversion will tie existing wells and predict depths accurately away from well control.
Notes: A prediction for an exploration reconnaissance well requires different effort than a prediction for a step-out well for a producing field. The geology will favor one method over another; no one method will provide optimum results everywhere. The availability of data immediately focuses the choice of methods: from only seismic velocities to the use of well data only. Time and budget are very real constraints. We need to choose methods wisely. A 1-day depth conversion will be different than a 6-month project; both can be done. The data and local geology will dictate the quality of the results.

## Slide 16: The Basic Methodology
QC & Analyze the Data
Determine Optimum T-D Method
Perform the Depth Conversion
Validate using Wells
Consider the Velocity Complexity
Notes: Here is the 5-step process we go through:
Look at your available data and check its quality.
Consider the velocity structure – simple layer cake geology to very complex.
Determine the optimum T-D method.
  This depends on things such as:
    Your business need
    Your available data
    The subsurface complexity
    The time/money/people available for this task
Perform the depth conversion.
Check the derived depths to known depths at wells to validate & perhaps make a correction.

## Slide 17: Which Velocity Data to Use
Well Velocities
Seismic Velocities
Advantages:
  High data density
  Vertical and horizontal info
  No well data needed
  Can be calibrated with well data
Advantages:
  Easy to interpret
  Detailed info at well location(s)
Disadvantages:
  Requires extensive processing
  Dix assumptions must be satisfied
  High quality analysis
  Resolution limitations
Disadvantages:
  Low data density
  Have to edit borehole artifacts
  Minimal lateral velocity changes
  No consideration for dip
  No info below well’s TD
Notes: Well data has two (2) advantages and several disadvantages. Seismic data has its advantages and disadvantages.

## Slide 18: Which Velocity Data to Use
Well Velocities
Well + Seismic Velocities
When to Use:
  Complex geology
  Significant lateral velocity changes
  Large study area when few wells
When to Use:
  Simple geology
  Minor lateral velocity changes
  Small study area with many wells
Examples:
  Time slice
  Horizon-based interval velocities
  Detailed velocity model
Examples:
  Constant function
  Depth slice
Notes: This slide gives examples of when to use well velocities and when to use well plus seismic data,

## Slide 19: Average or Interval Velocities?
Delta-T
Delta-T
If velocities increase steadily with depth,
Then try AVERAGE velocity methods
If velocities stair-step between mapped horizons,
Then try INTERVAL velocity methods
Notes: If velocities increase steadily with depth, then AVERAGE velocity methods may be adequate. If velocities stair-step between mapped horizons, then INTERVAL velocity methods might be needed.

## Slide 20: Time-to-Depth Conversion Methods
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake (Combinations of the above)
Increasing Complexity
Notes: Here are five (5) commonly used methods in order of complexity. We will briefly look at each one.

## Slide 21: Single, Constant Function
Delta-T
Delta-T
A single velocity function is used throughout the study area
Linear
Second Order
D = a + bT
D = a + bT + cT2
Simple, fast and cheap
OK for small areas with simple geology
Least accurate method
Notes: If the geology is rather simple with a consistent increase in velocity with depth and you don’t need a highly accurate prediction, then a single, constant velocity function should be adequate. The time-depth function can be linear or second order. Note the three (3) bullet points at the bottom of the slide.

## Slide 22: Time-to-Depth Conversion Methods
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake (Combinations of the above)
Increasing Complexity
Notes: Let’s discuss the Average Velocity Map method.

## Slide 23: Average Velocity Map
For a single horizon of interest, depth and time values are used at well locations to get average velocities
Average velocities at wells a gridded and contoured
Time map times Vavg map yields a depth map
1755 m
900 ms
2585 m
1220 ms
2380 m
1150 ms
2100 m
1050 ms
Well
A
Well
B
Well
C
Well
D
TOL Horizon
Depth & Time
For TOL horizon
1950 m/s
2120 m/s
2070 m/s
2000 m/s
Well
A
Well
B
Well
C
Well
D
Computed Average Velocities at Wells
1950 m/s
2120 m/s
2070 m/s
2000 m/s
Well
A
Well
B
Well
C
Well
D
1950
1950
2000
2050
2100
Average Velocities
gridded & contoured
[TWT Map] * [Velocity Map] / 2 = [Depth Map]
Notes: This method is done for one or more horizons of interest. A separate calculation is done for each horizon. We need the depth of the horizon in several wells and the corresponding TWT values. From the depth-TWT pairs (at well locations), we compute average velocities. Then, we grid and contour to get an average velocity map. Lastly, we multiply the TWT map by the average velocity map and divide by two (2) to get the horizon’s depth map.

## Slide 24: Time-to-Depth Conversion Methods
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake (Combinations of the above)
Increasing Complexity
Notes: We will now introduce Time/Depth Slices.

## Slide 25: Time/Depth Slices
Starting point is a good quality, high density velocity model
The seismic cube in time is sliced at constant time values at a small increment (e.g., every 400 ms)
Each slice is convert from time to depth based on the velocity model
The resulting time-depth relationships are used to transform the seismic cube from a vertical scale of TWT (ms) to depth (ft or m)
Notes: 1. We start with a good quality, high density velocity model.
2. We slice the TWT seismic cube at constant time values at a small increment.
3. Each time slice is converted to depth using the velocity model.
4. Given the time-depth relationships, we can transform the seismic cube from a vertical scale of TWT (ms) to depth (ft or m).

## Slide 26: Time/Depth Slices
Sea level
700 m
T = 1200 ms
T = 800 ms
T = 400 ms
1400 m
1300 m
2200 m
2100 m
Each slice is convert from time to depth based on the velocity model
Notes: For every sample in our 3D volume, we have an X, a Y, a TWT value and a corresponding depth value.

## Slide 27: Time-to-Depth Conversion Methods
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon-Keyed Interval Velocities
  Layer Cake (Combinations of the above)
Increasing Complexity
Notes: Moving down the list, we come to Horizon-Keyed Interval Velocities

## Slide 28: Horizon Keyed Interval Velocity
The starting point is a set of seismically-mapped sequence boundaries
Interval velocity data is analyzed sequence-by- sequence
The water layer is converted to thickness (depth) using a constant velocity value
The shallowest sequence is converted to thickness (in ft or m) by multiplying its isochron map by appropriate interval velocities; this thickness is added to the seafloor depth to get the depth of the base of the shallowest sequence
This process is continued sequence-by-sequence from shallow to deep
Notes: We start with a set of seismically-mapped sequence boundaries.
Interval velocity data is analyzed sequence-by-sequence
The water layer is converted to thickness (depth) using a constant water velocity value.
The shallowest sequence is converted to thickness (in ft or m) by multiplying its isochron map by appropriate interval velocities. This thickness is added to the seafloor depth to get the depth of the base of the shallowest sequence.
This process is continued sequence-by-sequence from the shallowest to the deepest interval.

## Slide 29: Horizon Keyed Interval Velocity
Layer 1
Vint = 1675 m/s
Water column
Vint = 1500 m/s
Layer 2
Vint = 1735 m/s
Layer 5
Layer 4
Layer 3
T
I M E
0
Notes: This cartoon cross-section illustrates the method. There are six (6) horizons (including sea level) that define five (5) intervals. In the simplest case, each interval is assigned a constant velocity. The easiest to define is the water column with an interval velocity of 1500 m/s (5000 ft/s). The water thickness in ms times 1500 gives the thickness of the water later in meters. In like fashion, the thickness in meters can be calculated for the four (4) other layers. The depth for each horizon can be obtained by adding the layer thickness for all the intervals above the horizon of interest, e.g., the top of the yellow horizon equals the sum of the thicknesses for the water layer, the tan layer, the grey layer and the green layer.

## Slide 30: Horizon Keyed Interval Velocity
T
I M E
0
Water Thick (s) * 1500 = Water Thickness (m)
0
D
E P T H
Depth of Water Bottom
0
D
E P T H
Depth of Layer 1 Base
Layer 1 Thick (s) * 1675 = Layer 1 Thick (m)
Layer 1
0
D
E P T H
Depth of Layer 2 Base
Layer 2
Layer 2 Thick (s) * 1735 = Layer 2 Thick (m)
Layer 1
0
D
E P T H
Depth of Layer 3 Base
Layer 3
Layer 3 Thick (s) * 1810 = Layer 3 Thick (m)
Layer 2
Layer 1
0
D
E P T H
Depth of Layer 4 Base
Layer 3
Layer 2
Layer 1
Layer 4
Layer 4 Thick (s) * 1885 = Layer 4 Thick (m)
Notes: This slide gives the formulas for the thickness in meters for each layer. By adding the thickness of each layer, we can build a cross-section with a vertical scale of meters.

## Slide 31: Time-to-Depth Conversion Methods
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake (Combinations of the above)
Increasing Complexity
Notes: The fifth method we will discuss is what is called the layer cake method.

## Slide 32: Layer Cake Method
This is the section we will work in the exercise
Several horizons define a number of “layers”
The method used for each layer can differ, depending on what is most appropriate
For example, the water layer can be converted from time to depth assuming a single interval velocity
However, deeper layers have a large range to TWT/depth and important lithologic changes; they have significant lateral changes in interval velocity that should be taken into account for reliable depth conversion

## Slide 33: Time-to-Depth Conversion Methods
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake (Combinations of the above)
  Advanced Methods
Increasing Complexity
Dense Velocity Analysis
Post-stack Depth Migration
Pre-stack Depth Migration
Tomographic Analysis - Image Ray Tracing
Notes: We have consider five (5) T-D conversion methods. There are more advanced methods that are beyond the scope of this lesson. Four (4) advanced methods are listed here. These give much more precise depth predictions, but they require more time, money and people specialized in doing these types of analyses.

## Slide 34: Depth Calibration
- 40
- 65
+170
What is the correction at the new drill location?
Mistie Map: Well Depth - Seismic Depth
You have three wells, with known amounts of mistie
Anyone can fix the misties by using a simple flex
The real interpretation questions are:
What is causing the mistie error and
What mistie value should I use at the new drill location?
Notes: Once you have done a depth conversion, you will what to calibrate your depth model using available wells (if you have any in your area). For example, let’s say you have three (3) wells in your area with depths for the TOL unconformity. You need a depth prediction for the TOL at a new drill location (red dot). You can look at the mistie at the existing wells, the well depth minus the depth from your T-D conversion of the TOL horizon. The simple solution is to apply a surface flex – an adjustment to your depth predictions so that you get no mistie at the three wells. The simple flex may be good enough, but a good interpreter would want to understand what caused the mistie error and how to use this knowledge to apply a geologically sound correction, at least at the new drill location.
Anyone can tie the wells by a simple flex. The real interpretation question is what is causing the error and what value should I use at my new drill location?

## Slide 35: Depth Calibration
Step 1: Calculate the mistie between the depth on the horizon in the well and the predicted depth from your T-D conversion
Step 2: Analyze the cause of the misties. They could be interpretation error, interpretation resolution, or misinterpreted well markers
Step 3: Make appropriate corrections so as to minimize the misties. Repeat Steps 1 and 2
Step 4: Edit the mistie map so that it reflects your understanding of the errors in a geologically reasonable manner
Step 5: Correct for any residual mistie by flexing to the well control
Notes: Here is a 5-step process for doing a depth calibration. This can only be done if you have wells in your area.

## Slide 36: Summary: Time-Depth Conversion
Time/depth conversion is important throughout the exploration/development/production cycle. Inaccurate depth conversions can lead to poor business decisions.
Integration of geologic knowledge is the key to a good depth conversion - what geologic factors control the subsurface velocity structure?
Use the optimal time/depth method based on the local geology and the data you have available
    For compaction controlled velocities, use a single function, Vavg maps, or time slices
    For areas with complex velocity fields due to structuring or the presence of high velocity rocks (carbonates, salt, volcanics), use horizon-keyed interval velocity or layer cake methods

## Slide 37: Time for an Exercise
Notes: Let’s do a simple exercise in which you will use the layer cake method.

## Slide 38: A Seismic Traverse
NW
SE
NW
SE
BARRACOUTA
Notes: The map on the left is a basemap for a 3D seismic survey. The white line indicates the location of the seismic line on the right. Note that the line is a random traverse that cuts perpendicularly across the anticline (not an inline or crossline).
On the seismic line we have six (6) horizons from the seafloor to the TOL – the Top of Latrobe unconformity (magenta). (There are three (3) deeper horizons that we do not use in this exercise.)

## Slide 39: Velocity Semblance at Location D
4500
0
1.000
0.800
0.000
0.600
0.200
0.400
3000
1500
Water Layer
Lakes Ent.
Seal
Miocene
Pleistocene
U. Plio
L. Plio
Velocity (m/s)
TWT (s)
Velocity = TWT * 860 + 1500
Notes: This is a velocity semblance display for location D. Hot colors indicate a good seismic stack, so a relatively good velocity at different depths. The straight dashed line is reasonable fit to the semblance data. This gives us an equation for average velocity as a function of depth.

## Slide 40: Time – Depth Comparison
Two-Way Time Section
Single Time-Depth Function
Based on a Single Velocity Function
Velocity = TWT * 860 + 1500
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake
Notes: On the left is the seismic traverse in TWT with the six (6) horizons displayed. On the right is a section in depth based on the velocity equation derived on the previous slide. The general horizon shapes are the same – a “stretch” as a function of depth has been applied to convert the vertical scale in meters. This is the Single, Constant Function method

## Slide 41: Velocity Semblance at Location D
4500
0
1.000
0.800
0.000
0.600
0.200
0.400
3000
1500
Water Layer
Lakes Ent.
Seal
Miocene
Pleistocene
U. Plio
L. Plio
Velocity (m/s)
TWT (s)
Chart: 
| 1500.0 | 1500.0 | 1540.0 | 1540.0 | 1560.0 | 1560.0 | 1600.0 | 1600.0 | 4300.0 | 4300.0 | 1700.0 | 1700.0 | 2200.0 | 2200.0
 | 0 | -0.079 | -0.08 | -0.239 | -0.24 | -0.354 | -0.355 | -0.529 | -0.53 | -0.779 | -0.78 | -0.939 | -0.94 | -1.1
Carbonates
Water
5000
0
1000
2000
3000
4000
Pleisto
U Plio
L Plio
Miocene
Lakes Ent.
Latrobe
Interval Velocity
By Sequence
Notes: Here is the same semblance diagram with a linear fit (black dashed line). We will define an average interval velocity for each interval/sequence defined by the six (6) horizons. Note the anomalously fast velocities for the Miocene, which is due to a mix of carbonates and clastics.

## Slide 42: Simple Layered Velocity Model to TOL
W
E
Chart: Velocity by Sequence
| 1500.0 | 1500.0 | 1540.0 | 1540.0 | 1560.0 | 1560.0 | 1600.0 | 1600.0 | 4300.0 | 4300.0 | 1700.0 | 1700.0 | 2200.0 | 2200.0
 | 0 | -0.079 | -0.08 | -0.239 | -0.24 | -0.354 | -0.355 | -0.529 | -0.53 | -0.779 | -0.78 | -0.939 | -0.94 | -1.1
1500 m/s
1540 m/s
1560 m/s
1600 m/s
4300 m/s
1700 m/s
2200 m/s
Carbonates
Water
5000
0
1000
2000
3000
4000
Pleisto
U Plio
L Plio
Miocene
Lakes Ent.
Latrobe
6
5
4
3
2
1
6
5
4
3
2
1
Notes: We can use interval thicknesses and interval velocities to get the thickness of each layer in meters. Then the depth to each horizon can be calculated by summing up the layer thicknesses down to each horizon.

## Slide 43: Time – Depth Comparison
Two-Way Time Section
Simple Layered Velocities
per Sequence
  Single, Constant Function
  Average Velocity Map
  Time/Depth Slices
  Horizon Keyed Interval Velocity
  Layer Cake
Notes: On the left is the seismic traverse in TWT with the six (6) horizons displayed, as on slide 40. On the right is a section in depth based on the thickness and interval velocity of each layer at each location. This is the Horizon Keyed Interval Velocity method in which a single interval velocity was used for each layer. This is more than a simple rescaling. The horizon geometries have changed. Note how thick the Miocene interval is (purple to orange). This is due to the much faster velocities for the Miocene rocks due to the presence of carbonates.

## Slide 44: Time – Depth Comparison
Single Time-Depth Function
Based on a Single Velocity Function
Simple Layered Velocities
per Sequence
This model does not contain any lateral changes in velocity
Notes: On the left is the depth model based on the single velocity vs. depth equation (slide 40). On the right is a depth model using layers in which each layer has a single interval velocity (slide 43). The display on the right has been adjusted so that depths of 0 and 1600 m are aligned. Note how wrong the depths to the magenta horizon (TOL unconformity/top of reservoir) are on the left display.

## Slide 45: Detailed Velocity Model
W
E
1500 m/s
1540 m/s
1560 m/s
1560 m/s
4450 m/s
1775 m/s
1500 m/s
1540 m/s
1680m/s
1720 m/s
3550 m/s
1525 m/s
No Lateral Change
No Lateral Change
Increases Downdip
Increases Downdip
Decreases Downdip
Decreases Downdip
Less Carbonate
Less Terrigenous
Notes: There are important lateral velocity changes for each sequence in this area. In the exercise, you will use these laterally varying interval velocities to get the depth of the horizons, with emphasis on the magenta (top of reservoir) horizon.

## Slide 46
Questions?