## Slide 1: Petroleum Geology & Geophysics
Seismic Inversion
-1
*
Wavelet
Blocked Impedance
Actual Trace
Blocked Velocity
Blocked
Density

## Slide 2: Objectives
Comparison between zero phase and impedance data
Our ultimate goal
Relative impedance
Absolute impedance
Low frequency component
Basic inversion process
Notes: Six main topics within this lecture.

## Slide 3: A Quick Review
Marine Shale
Shoreface Sand
Marine Shale
Marine Shale
Shoreface Sand
Fluvial Sand
Zero Phase Trace
Zero Phase – used to identify and map major changes in impedance
Relative Impedance
Trace
Relative Impedance – used to quantify properties above/below major impedance boundaries
A
B
Notes: Here we have some marginal marine parasequences with shoaling upwards lithofacies. The major jumps in impedance occur at the boundaries marked by the magenta and purple lines. The zero phase responses are peaks centered on these large impedance changes (shales over sands).
Relative impedance is an estimate of the impedance units – here the sands are higher impedance than the shales. Thus, relative impedance is more of an interval attribute than an impedance “break” property. The two peaks can tell me something about the two sandy intervals A and B.

## Slide 4: Forward Seismic Modeling
The Convolution Model
Blocked Logs
Refl. Coef.
Modeled Trace
Wavelet
*
A Unique Solution
Input is a sonic log and a density log
It is performed at well locations
It allows us to tie well markers to the seismic trace
Well data can be modified to understand the seismic signature of lateral variations (e.g., what if the reservoir was twice as thick)
Notes: More review, the convolutional model. We covered this when talking about making a synthetic seismic trace from sonic and density logs. The geology at the well location, based on the log responses and a given pulse, leads to a unique solution – a single modeled trace.

## Slide 5: Inverse Seismic Modeling
Seismic Inversion
Non-unique Solutions
-1
*
Wavelet
Blocked Impedance
Actual Trace
Blocked Velocity
Blocked Density
Input is any seismic trace
It is performed away from well locations
Well data can be used to calibrate the results
It can help us understand what the seismic is telling us about rock properties (velocity and density)
Software can generate multiple realizations of the velocity and density, range of possibilities
Notes: Inverse seismic modeling starts with a seismic trace, either at a well location or away from any wells. We use an extracted or assumed wavelet. We derive an impedance curve that could have generated the observed seismic trace. The impedance curve is non-unique – there are several ways the impedance curve can be modified and still get the observed trace. As a simple example, any particular peak or trough could be due to only a change in velocity, only a change in density, or the combined effect of both a change in velocity and density.
Sometimes we go another step (beyond estimating the impedance). There are methods we can use to estimate the P-velocity, the S-velocity and the density.

## Slide 6: The Ultimate Goal
Ideally, we would like to turn each seismic trace into an impedance trace or, going even further, into a velocity and density pseudo-log
That would allow us to predict rock properties in an interval of interest rather than acoustic properties at a major rock boundary
Variations in velocity and density at each seismic trace would be better indicators of lateral changes in rock properties, such as thickness, net:gross or porosity
Notes: Our ultimate goal is to turn each seismic trace into an impedance trace or, going further, into a velocity and density pseudo-log. That would allow us to predict rock properties in an interval of interest. Variations in velocity and density at each seismic trace would be better indicators of lateral changes in rock properties, such as thickness, net-to-gross or porosity.

## Slide 7: Definition
Seismic inversion is the process that starts with a reflection amplitude trace, generates a model for the impedance structure that produced that trace and then transforms the impedance into estimates of Vp, Vs and density
It is an inverse of the convolution method that we use to model a seismic trace from a sonic log and a density log

## Slide 8: Relative Impedance
Since the input zero phase trace has a limited frequency range, the derived relative impedance is also band-limited
It is relatively easy to derive from a zero phase trace by two methods:
  Integrating the zero-phase trace (a running sum)
  Rotating the phase of the zero-phase trace by -90°
Zero Phase Trace
Relative Impedance
Trace
Phase Rotation
Trace Integration
or
Notes: Since the input zero phase trace has a limited frequency range, the derived relative impedance is also band-limited. It is relatively easy to derive from a zero phase trace by two (2) methods: (1) Integrating the zero-phase trace (a running sum), and (2) the phase of the zero-phase trace by -90°.

## Slide 9: The Major Difference
Two-Way Time (ms)
Impedance Log
Relative Impedance Units
Two-Way Time (ms)
Chart: 
-150
-100
0
-50
250
200
100
50
150
1000
1050
900
950
800
850
700
750
650
Relative Impedance lacks the low frequency trends and the high frequency oscillations
Based on Chopra and Sharma, 2012
Notes: On the left is an impedance log for a well (sonic * density). Note that it is rich in frequency, from low frequency trends to high frequency oscillations. A simple inversion of the seismic trace at the well location gives us relative impedance – it lacks the very low and very high frequencies. The magenta arrows highlight the low frequency trends seen in the impedance log. We would like to add these low frequency trends to the impedance estimate.

## Slide 10: Limitation of Relative Impedance
  Due to bandwidth limitations, relative acoustic impedance from seismic provides only an approximation of acoustic impedance as seen on logs
  If we go to the extra trouble to restore the missing low seismic frequencies (< 10 Hz) we can calculate absolute impedance, which provides a better fit to log data
Notes: The limitation of relative impedance is that it has only the frequency content of the input zero phase data – typically 10 to 40 or 50 Hz. Thus, it lacks the very low and very high frequency information that we see in an impedance log. There are methods by which we can estimate and add in the very low frequency information.

## Slide 11: Frequency Content
Two-Way Time (ms)
Impedance Log
Sonic and density logs have a wide range of frequencies, from 0 to 200+ Hz
Zero Phase Trace
Relative Impedance
Trace
A seismic trace has a limited range of frequencies, about 10 to 50 Hz
Relative impedance will have the same limited range of frequencies as the trace it was derived from
Notes: This slide reemphasizes the previous slide. The impedance log has a frequency range of 0 to 200+ Hz. The zero phase trace has about 10 to 50 Hz. Since relative impedance is derived from the zero phase trace, it is also limited to the 10 to 50 Hz frequency range.

## Slide 12: Two Types of Impedance Data
  Relative Acoustic Impedance
    A simple mathematical integration of zero phase seismic reflectivity data or a -90° phase rotation
    Indicates relative changes (+/-) in seismic impedance
    In some cases can be calibrated locally to an average physical property of a reservoir unit
    Not useful for accurately measuring vertical impedance changes over large intervals
Notes: There are two (2) types of impedance data we can estimate and use:
- relative impedance (this slide), and
- absolute impedance (next slide).
Slide 8 outlined how we get relative impedance: (1) Integrating the zero-phase trace (a running sum); and (2) rotating the phase of the zero-phase trace by -90°. Relative impedance indicates relative changes (increases/decreases) in seismic impedance. In some cases, it can be calibrated locally to an average physical property of a reservoir unit. Since it lacks the low frequency trends, it is not useful for accurately measuring vertical impedance changes over large intervals.

## Slide 13: Two Types of Impedance Data
  Absolute Acoustic Impedance
  Begins with relative impedance, which was described on the previous slide
  Restores low frequency component of seismic data using:
    Well data from the project area, and/or
    Seismic derived stacking velocities (from processing)
  Precise calibration of impedance measurements is possible for multiple reservoirs at multiple well locations
  Frequently it is used to build input for a detailed reservoir model (for reservoir simulation)
Notes: Absolute impedance is much more informative. We start with the relative impedance, which was described on the previous slide. We estimate and restore the low frequency component of seismic data using: well data from the project area, and/or seismic derived stacking velocities (from the data processors). Precise calibration of impedance measurements is possible for multiple reservoirs at multiple well locations. Frequently, it is used to build input for a detailed reservoir model (for reservoir simulation).

## Slide 14: Low Frequencies from Stacking Velocities
The hotter colors indicate the velocities that result in a good flattening of gathers
The blue “Xs” are the values that the velocity interpreter selected
The red block curve show the computer interval velocities
Velocity
Two-Way Time
Vint
The gradual increase in velocity with depth is what we use to get the low frequency trends in impedance
Notes: This is called a semblance diagram. The colors indicate how well a seismic gather is flattened at different velocities as a function of depth (TWT). A velocity analyst will draw a curve (magenta line) to define a velocity vs depth function for this gather. This velocity function gives us an estimate of the low frequency component at the CMP location of this gather.

## Slide 15: Frequency Spectra
Frequency
Amplitude
0
10
20
30
40
50
60
70
80
0
100
50
Seismic
Bandwidth
LOW FREQUENCY COMPONENT
Notes: Using this frequency spectra diagram, we get the red seismic bandwidth information from the zero phase trace. We estimate the low frequency component either from filtering log data or using stacking velocities. By adding the two together, we get a better representation of the impedance structure at various locations.

## Slide 16: Acoustic Impedance Data
  Estimates impedance/sonic/density log responses from migrated and stacked seismic traces
  Is an interval attribute, as opposed to an interface property
  Can better resolve beds that are thinner than tuning thickness than with zero phase data
  Useful as a lithology or porosity indicator
  In some cases reveal HC/water contacts better than with zero phase data
  Commonly is used for pore pressure prediction
Notes: Several facts about the acoustic impedance data.

## Slide 17: Impedance Data: Value
  It represents the subsurface better, especially when low frequency information is included:
        Low frequency geologic variations
        Increased vertical resolution
  It may yield better estimates of reservoir thickness
  It can be transformed to rock properties, such as net pay, porosity, hydrocarbon pore thickness
  It allows us to perform enhanced seismic attribute analysis
  Increasingly it is being used by interpreters to delineate reservoir rocks and surrounding seals
Notes: Some of the reasons that these data give us value.

## Slide 18: Assumptions for Post Stack Inversion
  The input seismic data has been imaged properly and is zero phase
  Seismic amplitudes are proportional to reflection coefficients (controlled amplitude and phase seismic processing)
  The input seismic data represents normal incidence (zero-offset) traces (AVO effects have not influenced the migrated/stacked data)
  Input data is free of multiples and coherent noise
  An appropriate wavelet has been extracted and it does not change with time
  We use a near offset stack as input if the S:N ratio is adequate
Notes: Several statements about our assumptions. Given point #3, we would prefer to use a near offset/angle stack to derive the impedance traces. The signal-to-noise ratio has to be adequate, removing most of the random noise. If S:N is low, then we would use the full stack zero phase data as our input to the inversion operation.

## Slide 19: Inversion Process
Seismic
Data
Well
Data
Sonic, Density Logs
Markers
Directional Survey
Check Shots
Zero Phase
Full, Partial Stacks
Stacking Velocities
Horizons
Horizons
Wavelet
Low
Frequency
Component
Filtered Logs
Stacking Velocities
INVERSION
Zero
Phase
P-Impedance
Density
S-Impedance
Lithology
Porosity
Notes: This slide walks through the inversion process. We start with seismic and well data, from which we can get horizons. We get the low frequency content from filtering logs or stacking velocity analysis. We also extract a wavelet from the seismic data. Using the zero phase data, the low frequency component and the wavelet, we invert the seismic data to get impedance and density. We can then try to develop a relationship to give us predictions of rock and fluid properties, such as lithology and porosity.

## Slide 20: Example 1
Modified from Russell and Hampson, 2006
A zero phase seismic line that shows a gentle structure with an amplitude anomaly that is caused by a gas field.
Horizon 1
Horizon 2
Horizon 3
Notes: We will show two examples. Example 1 is for a gas field. Here we show the zero phase data at two scales. There is an amplitude anomaly associated with the presence of the gas. Consider how much detail on the distribution of the gas is apparent on the zero phase data. We will show the inversion result for the zoomed in view (lower right).

## Slide 21: Example 1
Horizon 1
Horizon 2
Horizon 3
Modified from Russell and Hampson, 2006
A zoomed portion of the zero phase seismic line over a known gas field.
Horizon 1
Horizon 2
Horizon 3
An inversion of the seismic line based on a recursive type of inversion. Note how the gas field stands out.
Notes: The upper image is the same zero phase data as was on the last slide (lower right). On the bottom is the absolute impedance obtained from the inversion process. Note how much more detail there is about the reservoir unit and the gas “sweet spot” (cyan).

## Slide 22: Example 2
Modified from Misra and Chopra, 2011
A zero phase seismic line that intersects two wells. The P-impedance curves are shown in black.
50 ms
Well 1
Well 2
A P-impedance section. This was obtained with a probabilistic neural network.
1 km
50 ms
Notes: Here is a second example. Top view is the zero phase data; there are two P-impedance curves shown for two (2) wells. The three (3) arrows in well 1 and the one (1) arrow in well 2 mark pay zones. Note there is not a good correlation between the impedance curve (from well logs) and the zero phase reflection bands.
The lower view is the absolute impedance derived using a probabilistic neural network method. There is a reasonably good relationship between the impedance curves and the colors. Note how the pay zones are easier to identify.

## Slide 23: Example 3
An estimated P-wave velocity section obtained by a PNN analysis. The black curves are P-wave sonic logs.
An estimated density section obtained by a PNN analysis. The black curves are density logs.
50 ms
1 km
50 ms
Modified from Misra and Chopra, 2011
Notes: Going a step further, the impedance was broken down to estimates of P-wave velocity and density. Again, the pay zones are easier to identify.

## Slide 24: Summary
  Provides a log estimate at every single seismic trace
  Intervals are easier to interpret geologically than the interface properties that zero phase data measures
  Estimated acoustic impedance can be compared to well- derived acoustic impedance to calibrate the results
  Acoustic impedance can help us estimate lithology, porosity, fluid content, and pore pressure anomalies
  The inversion process attempts to remove the band- limiting effect of the seismic wavelet, hopefully providing increased geologic detail
  Geo-statistical data derived from well control can be combined with seismic impedance values to produce acoustic impedance volumes with improved vertical resolution
Notes: Summary Statements

## Slide 25: References
Slide 9: Chopra, S. and Sharma, R., 2012, A Solid Step towards Accurate Interpretations, AAPG Explorer, December, p. 36-37.
Slide 19-20: Russell, B. and Hampson, D, 2006, The Old and the New in Seismic Inversion, CSEG Recorder, V. 31, N. 10, December.
Slide 21-22: Misra, S. and Chopra, S., 2011l, B. and Hampson, D, 2006, Neural Network Analysis and Impedance Inversion – Case Study, CSEG Recorder, V. 36, April, p. 36-39.
Notes: Slide 29.25
Three references

## Slide 26
Questions?