## Slide 1: Exercise 29
Using Seismic Inversion
Using Seismic Inversion
Your Task:
  Consider how an absolute impedance trace is constructed and used to evaluate a reservoir interval.
  Impedance Curve
  Relative Impedance

## Slide 2: Introduction
You will work on data from Western Canada. A Triassic formation is composed of thick sandstone bodies that are encased in shales. Many of these sands have been found to be economic hydrocarbon reservoirs. The sands have higher impedance than the shales. In addition, there is a good correlation between higher impedance values and higher reservoir quality (a combination of greater sand thickness, higher net-to-gross and higher porosity).
Zero-phase seismic data, which concentrates on major impedance boundaries, was used to map the top of the formation. The data was transformed into relative acoustic impedance, which is used to evaluate an interval of interest, such as this reservoir zone.
You will examine the relative impedance trace at a well location and compare it with the well’s impedance curve. Then you will complete an absolute impedance trace and considers its value in evaluating this reservoir.
Notes: Introduction to the exercise.

## Slide 3: Step 2: The Relative Impedance Trace
Question:
Can you pick with confidence the zone of high impedance associated with reservoir-quality sand?
Chart: 
-150
-100
0
-50
250
200
100
50
150
1000
1050
900
950
800
850
700
750
650
Relative Impedance Units
Two-Way Time (ms)
Notes: The relative impedance trace from the 3D seismic volume at the well location. Can you pick with confidence the zone of high impedance associated with reservoir-quality sand? It is down near 1030 ms.

## Slide 4: Impedance Log & Relative Impedance
Relative Impedance Units
Two-Way Time (ms)
Impedance Values
Notes: On the left is the impedance “log” derived by multiplying values from the sonic log and the density log. On the right is the relative impedance trace from the seismic at the well location. Note the differences – relative impedance does not look like the impedance “log” since it lacks low frequency trends.

## Slide 5: Low Frequency Component
-150
-100
0
-50
250
200
100
50
150
Chart: 
Chart: 
1000
1050
900
950
800
850
700
750
650
920
1040
Notes: By filtering the impedance log, we obtain the low frequency component (0 – 10 Hz). The red box shows the portion of the diagram that is enlarged on the next slide.

## Slide 6: Step 4: Obtaining Absolute Impedance
+
=
Notes: If we take the relative impedance values and add the low frequency component, we get what is referred to as absolute impedance. Absolute impedance looks much more like the log-based impedance, which is our goal. We can invert every trace in the seismic volume to get an absolute impedance volume.

## Slide 7
Questions?