## Slide 1: Petroleum Geology & Geophysics
Estimating Ultimate Recovery
Latrobe Reservoir
Oil or Gas
Lakes Entrance Shale

## Slide 2: Outline
Overview
Gross Rock Volume
Reservoir Volume
Pore Volume
HC Volume
2

## Slide 3: Estimated Ultimate Recovery
Let’s say that you have defined a prospect that has a good chance of holding hydrocarbons (HCs)
A major question to answer is “What is the value in dollars of your prospect?”
Ultimately, you want to know if your company can make a profit, which is value of the recoverable HCs minus the cumulative costs
Thus, we need to estimate the EUR – the amount of oil/gas that we can get to the surface and sell
Notes: The WHY we want to do this. Definition of Estimated Ultimate Recovery.

## Slide 4: For Example
Latrobe Reservoir
Gas
Lakes Entrance Shale
Notes: This might be what we find when we drill the wildcat well. Now we want to know how much gas: 1) is in the reservoir, and 2) what volume we hope to get to the surface and then sell.

## Slide 5: Estimated Ultimate Recovery
Estimating ultimate recovery may seem to be a daunting task – it is!
We have to take it step-by-step
First, we estimate the HC that we think is within the reservoir at depth, no small task
Then, we can consider how much we might get to the surface (barrels of cubic feet of gas)
So how do we get HC in place?
Notes: This process may seem frightening. We will tackle it step-by-step. First, we estimate the HC that we think is within the reservoir at depth. Then, we can consider how much we might get to the surface.

## Slide 6: Obtaining HC in Place
We start by estimating the total volume of rock in our prospect
Then we reduce that volume step-by-step until we get an estimate of the volume of HC in the reservoir at reservoir conditions
Total Rock
Volume
Reservoir Sand
Volume
Non-Res
Non-Net
Non-Res
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
Notes: We go through a four (4) step process, summarized here. The next four (4) slides highlight these steps. Students will go through these estimates when working the exercise.

## Slide 7: Total Rock Volume
A first approximation:
  Map the areal extent of the trap (use a planimeter)
  Estimate how far down dip the HCs extend
  Convert the isochron map (ms) to an isochore map (m or ft) using velocity data from the well
  Combine the HC extent and the thickness to get a total rock volume (km3 or acre/ft)
Total Rock
Volume
Field Area
*
Aver. Thick
Total Rock Vol.
Notes: Step 1: Estimate the total rock volume of the newly discovered field. Basically, get an area and an average thickness. Computer tools exist that help get these numbers.

## Slide 8: Reservoir Rock Volume
A first approximation:
  Start with the total rock volume
  Estimate the net-to-gross for the reservoir interval (good sands versus waste rock)
  Net-to-gross (N/G) often varies by the environments of deposition
  For our field:
    N/G for shoreface = 80%
    N/G for delta plain = 65%
    N/G for fluvial = 50%
Total Rx Vol.
*
Net-to-Gross
Res. Rock Vol.
Reservoir Sand
Volume
Non-Res
Non-Net
Non-Res
Notes: Step 2: Estimate the RESERVOIR rock volume. Multiply the total volume by the net-to-gross.

## Slide 9: Pore Volume
Res. Sand Vol.
*
Porosity
Pore Volume
A first approximation:
  Start with the reservoir sand volume
  Use a porosity value (percentage of volume that represents the pore space)
  Porosity often varies by the environments of deposition
  For our field:
    Φ for shoreface = 20%
    Φ for delta plain = 18%
    Φ for fluvial = 16%
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Notes: Step 3: Estimate the PORE volume. Multiply the reservoir sand volume by the porosity.

## Slide 10: Hydrocarbon Volume
A first approximation:
  Start with the net pore volume
  Use a HC saturation value (e.g. 80% HC saturation means 80% of the pore space contains HCs, the other 20% has irreducible water)
  For this field, we will assume a HC saturation of 90%
Net Pore Vol.
*
HC Saturation
HC Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
Notes: Step 4: Estimate the HYDROCARBON volume. Multiply the pore volume by the HC saturation value.

## Slide 11: Recoverable HC
We need a recovery efficiency to go from HC in place to recoverable HC
To get a recoverable gas value, we will assume a 70% recovery efficiency
Many factors go into recovery efficiency, in particular, how effective the reservoir’s “plumbing” is (permeability)
We also include a volumetric expansion due to the drop in temperature and pressure
In-Place HC
*
Recovery Eff.
*
Expan. Factor
Recoverable V.
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
In Place
at Depth
Volume Recovered
at Surface
Gas
Expansion
Notes: Now we need to consider how much we can get to the surface (recoverable volumes). There are two (2) main factors:
(1) We typically recover only a small percentage of oil; a higher percentage of gas. A lot of reservoir engineering
goes into recovery efficiency; beyond the scope of this course.
(2) The HC expands at it goes from reservoir temperature & pressure to surface temperature and pressure.
We multiply in-place HC volume by the recovery efficiency number and the expansion factor.

## Slide 12: Time for an Exercise
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
In Place
at Depth

## Slide 13: Lecture 30
Questions?
Notes: Slide 30.13