## Slide 1: Exercise 30a: Estimating Ultimate Recovery
Estimating Ultimate Recovery
Your Task:
  Develop a most likely, minimum and maximum volume of gas that can be brought to the surface and sold.
Time Thickness
in ms
Notes: A review of exercise 30a.

## Slide 2: Computation Sheet
2
Most-Likely = 3.7 TCF, but could be 1.7 to 6.1
ROW | PARAMETER | Most Likely Case | Low-Side Case | High-Side Case
1 | Area (in sq km) | 90 | 70 | 105
2 | N:G * Porosity | 0.12 | 0.11 | 0.13
3 | Gross Thickness in kilometers | 0.14 | 0.12 | 0.15
4 | HC Saturation | 0.9 | 0.8 | 0.95
5 | HC Pore Volume in cubic kilometers | 1.361 | 0.739 | 1.945
6 | Recovery Efficiency | 0.7 | 0.6 | 0.8
7 | Recoverable Gas Reservoir Conditions in cu. Km | 0.953 | 0.444 | 1.556
8 | Recoverable Gas at Surface in Billon cubic meters | 105.73 | 49.23 | 172.73
9 | Recoverable Gas at Surface in Bcf | 3732 | 1738 | 6097
Notes: This is the computation sheet filled in with my number. Students’ numbers should be close – does not have to be exact. Management is interested in all three (3) numbers on the bottom. In this case, I estimate the most likely to be on the order of 3.7 TCF (trillion cubic feet). It could be as small as 2 TCF or as large as 6 TCF. The wide range in values indicates how little we know about the input parameters with only one (1) well and the seismic data

## Slide 3: HC Pore Thickness
3
3
HC Pore
Thickness
Meters
Colors indicate HC pore thickness in meters
(gross thickness * N:G * Φ).
Contours are gross thickness of the gas-bearing reservoir.
Notes: This map was generated by using the seismic to get maps of each of the input parameters. Grid operations were used to derive a most-likely value for HC pore thickness at each shot point.
HC pore thickness = how tall a gas column would be if all the sediments were removed – physically (not practical, but very informative). Hot colors indicate where the greatest quantity of gas should be found.

## Slide 4
4
Questions?
Notes: 4
Slide SOLU Ex-30a.4