## Slide 1: Petroleum Geology & Geophysics
Development Geology & Geophysics
Time
Early in the
Business Cycle
Late in the
Business Cycle
Regional
Compartment-Scale
Reservoir-Scale
Prospect-Scale
Block-Wide
Scales of Analysis
1. Capture
3. Initiate
4. Deplete
2. Discover
Abandon/Sell
Exploration
Development
Production

## Slide 2: An Asset’s Life Cycle
Capture Opportunities
Discover Hydrocarbon
Initiate Production
Deplete the Field
New Ventures
Exploration
Development
Production
Notes: Review – an asset’s life. In this lecture, we will focus on the field development stage.

## Slide 3: Changes with Business Stage
Time
Early in the
Business Cycle
Late in the
Business Cycle
Regional
Compartment-Scale
Reservoir-Scale
Prospect-Scale
Block-Wide
Scales of Analysis
1. Capture
3. Initiate
4. Deplete
2. Discover
Abandon/Sell
Geoscience
Production &
Engineering
Information & Effort
Info
Effort
Exploration
Development
Production
Notes: This chart shows how things change over the life of a asset. The scale of the analysis progressively zooms in from regional to individual compartments within a producing field. Geoscience information always increases. Geoscience effort peaks in the early production stage. Information on production and engineering is minimal during exploration; it becomes more and more significant until the field is near abandonment.

## Slide 4: Phase 1
Capture Opportunities
To Recognize HC Potential and Capture Acreage
BASIN-SCALE ANALYSIS
Local Wells and Seismic
Adjacent Wells & Seismic
Analogy Areas
Tectonic Setting
Well-Seismic Ties
Structural Framework
Stratigraphic Framework
PRODUCTS:
Play Adequacy Maps
Initial Leads
Preliminary Assessment
Risk and Rank
Bidding Strategy
Review
Notes: This slide reviews the analysis and products associated with the early exploration phase – where we want to capture opportunities.

## Slide 5: Phase 2
To Define Drillable Prospects and Discover HCs
Discovery Hydrocarbons
BLOCK-SCALE ANALYSIS
Denser 2D or 3D Seismic
Refined Well-Seismic Ties
Refined Faults
Refined Horizons
EOD Interpretations
Geochemical Models
DHI & AVO Analysis
Time/Depth Conversion
PRODUCTS:
Screen Leads
Assess Prospects
Volumetric Analysis
Risking & Ranking
Wildcat Well(s) Strategy
Post-Drill Evaluation
Review
Notes: This slide reviews the analysis and products associated with the mid to late exploration phase – where we want to discovery HCs.

## Slide 6: Phase 3
To Determine HC Distribution and Predict HC Flow
Initiate Production
RESERVOIR-SCALE ANALYSIS
Enhanced Seismic Data
New Wells Tied to Seismic
Detailed Mapping
Calibrated Attributes
Seismic Modeling
Build Geologic Model
PRODUCTS:
Reservoir Architecture
Reservoir Simulation
Initial Development Plan
Project Funding
Early Production Wells
First Oil/Gas
Revised Model/Plans
Development G&G
Notes: This slide reviews the analysis and products associated with the field development stage – where we want to initiate production from a new field. We will talk about some of these types of analysis and their products in this lecture, but only scratch the surface.

## Slide 7: To Develop a Newly Found Field
To develop a field, we need a refined understanding of the reservoir:
1. Its area, thickness, volume
2. Its internal architecture, and
3. How it is broken into separate compartments to be produced
Discovery Well
Confirmation Well
Reservoir Map at the end of the Exploration Phase
Reservoir Map at the end of the Development Phase
Development
Wells
Exploration
Wells
Notes: To develop a newly discovered field, the three (3) big things we need to determine are:
- The area and thickness of the oil or gas reserves so we can estimate the volume.
- The internal architecture of the reservoir rocks.
- How the reservoir is broken into separate compartments to be produced.

## Slide 8: We May Need Better Data
Data Used for Exploration
Data Reprocessed or
Reshot for Development
and Production
Notes: Transitioning from exploration to development, we may need better seismic data. This is because we need more detail – better imaging and higher resolution. One way to get better data is to reprocess the existing seismic data using higher-end processing methods. We may have to acquire new seismic data. If exploration had only 2D seismic, a 3D survey would probably be needed.

## Slide 9: The Discovery
BARRACOUTA-1:
  Drilled on the crest of a major anticline
  A sub-unconformity trap was predicted
  Only poor-quality 2D seismic data
  Found:
    100 meters of gas
    13 meters of oil
Line 60
Line 69
Line 66
Line 63
Line 75
Line 72
Line 10
Line 14
Line 18
Line 22
Line 26
1000
1000
900
1000
1100
1200
1100
1300
1200
1300
1400
1500
1600
N
Time Structure Map
in milliseconds
Discovery
Well
Review
Notes: A review of what we have done in this course on the Barracouta-1 wildcat.

## Slide 10: The Exploration Phase
Our company acquired three (3) blocks containing a large anticlinal lead
This lead was matured to a drillable prospect using a grid of 2D seismic lines
A successful wildcat well was drilled
Four (4) field delineation wells were drilled
A 3D seismic survey was designed, approved, acquired and processed
Review
Notes: A review of the exploration phase.

## Slide 11: What’s Next
With the drilling of the field delineation (confirmation) wells, the exploration phase typically ends
This asset would be passed along to development geoscientists
Normally some of the explorationists who worked the field discovery and delineation would transfer to the production group/department/company
We will continue our story of the Barracouta Field in the next two (2) lessons
Notes: Some likely next steps. NOTE: For super-majors, there may be separate companies for exploration and production, where mid-size and smaller companies may have two groups.

## Slide 12: Lecture 31
Questions?