## Slide 1: Exercise 32b
Design & Place a Platform
Your Task:
  Use a HC-pore thickness map to answer four (4) early development questions based on some simple economic factors.
0 km 2
HC Pore
Thickness
Meters
Notes: Slide Ex-32b.1
Title slide with main task.

## Slide 2: Introduction
Since your team of geoscientists worked long and hard on the newly-discovered Barracuda Field, you have been asked for your recommendations for the initial field development plan.
You only need to consider geosciences issues along with simple economic assumptions.
Others are looking into engineering, legal, taxation, and other non-geoscience issues.
There are four (4) main questions for you to address (next slide).
Notes: Background to the exercise.

## Slide 3: Main Questions
How many platforms do we need to maximize production while minimizing costs, so that we maximize profits: one, two or three?
What is the surface location for the platform or platforms?
How many production wells should we plan for each platform?
Where at the reservoir depth should we target each proposed production well?
Notes: Background to the exercise.

## Slide 4: An Important Constraint
An important constraint is the “reach radius” for these platforms.
We will assume that a well can target a location at the top of the reservoir that is anywhere within a radius of 2 km from the platform’s surface location.

## Slide 5: Introduction
Some necessary numbers and conversion factors:
5
Area of Each Cell on Map | 0.8 sq km
Recovery – Central Cell | 80%
Recovery – 6 neighboring Cells | 40%
Gas Expansion Factor | 111 scm/rcm
Energy | 36x106 mmBTU/cu km
Exploration Costs | $50 million
Development Costs | $75 million

## Slide 6: Suggested Approach
6
As a team, come up with three (3) or four (4) possible production plans worth evaluating. Then have each team member run a cost analysis for one of these plans so that you have three (3) or four (4) possible production plans and the value and cost of each for comparison. Decide on which option is most appealing (biggest profit) and prepare a brief report on just that one case.
For example, one plan might be a single platform with one well. For this case, you would position the platform above the cell with the largest HC pore thickness. One team member would first estimate the value of the gas (ending in $M) and then estimate the total costs; exploration, development, facilities (platform & well), and operating costs for 25 years. Value minus total costs would be the profit (or loss).

## Slide 7: Suggested Approach
7
The seven steps in the exercise will take you through:
  1. The estimation of the value of the gas,
  2. The costs associated with a development plan (N platforms with a total of M wells), and
  The profit (or loss).
We will look at the map and go through an example calculation together

## Slide 8: Hydrocarbon (HC) Pore Thickness
0 km 2
Contour interval = 3m
HC Pore
Thickness
Meters

## Slide 9: HC Pore Thickness
0 km 2
Reservoir divided into cells = 0.8 km2
HC Pore
Thickness
Meters

## Slide 10: HC Pore Thickness
0 km 2
Average HC pore thickness values for each cell
6
2
2
1
8
7
2
1
2
2
1
3
4
1
5
4
5
1
3
7
2
2
6
5
10
8
3
5
11
8
6
5
8
7
7
8
8
9
8
3
2
8
13
14
7
3
6
15
14
10
2
4
16
13
12
2
3
17
12
13
1
3
16
10
14
2
3
16
10
14
4
2
14
9
13
5
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1
HC Pore
Thickness
Meters

## Slide 11: Your Map for Exercise 25
6
2
2
1
8
7
2
1
2
2
1
3
4
1
5
4
5
1
3
7
2
2
6
5
10
8
3
5
11
8
6
5
8
7
7
8
8
9
8
3
2
8
13
14
7
3
6
15
14
10
2
4
16
13
12
2
3
17
12
13
1
3
16
10
14
2
3
16
10
14
4
2
14
9
13
5
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1
0 km 2
Average HC pore thickness values for each cell
2 km
A
B
C
J
I
E
D
H
G
F
K
M
L
R
Q
P
O
N
X
W
V
U
T
S
A
B
C
J
I
E
D
H
G
F
K
M
L
R
Q
P
O
N
X
W
V
U
T
S
1
2
2
1
3
Lateral reach for wells

## Slide 12: Example Calculation
0 km 2
Average HC pore thickness values for each cell
Platform at Eastern Edge
Surface Position = V-2
Wells Target U-3 and W-2
6
2
2
1
8
7
2
1
2
2
1
3
4
1
5
4
5
1
3
7
2
2
6
5
10
8
3
5
11
8
6
5
8
7
7
8
8
9
8
3
2
8
13
14
7
3
6
15
14
10
2
4
16
13
12
2
3
17
12
13
1
3
16
10
14
2
3
16
10
14
4
2
14
9
13
5
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1
A
B
C
J
I
E
D
H
G
F
K
M
L
R
Q
P
O
N
X
W
V
U
T
S
A
B
C
J
I
E
D
H
G
F
K
M
L
R
Q
P
O
N
X
W
V
U
T
S
1
2
2
1
3

## Slide 13: HC Thickness at Each Well
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1
R
X
W
V
U
T
S
R
X
W
V
U
T
S
2
1
Well A
Well B
Each well can partly drain:
The central cell at 80% recovery
The neighboring 6 cells at 40%
Well A:
6 * .8
(5+5+4+4+8+8) * .4
Equals 4.8+ 13.6 = 18.4 m
Equals 0.0184 Km
Well B:
2 * .8
(1+1+1+1+5+2) * .4
Equals 1.6 + 4.4 = 6 m
Equals 0.006 km
Step 2a, 2b, 2c

## Slide 14: HC Volume at Each Well
R
X
W
V
U
T
S
R
X
W
V
U
T
S
2
1
Well A
Well B
Gas Volume = area * thickness
Cell area = 0.8 km2
We will use units of km3
Well A:
Area = 0.8 km2
Thickness = 0.0184 km
Volume = 0.0147 km3
Well B:
Area = 0.8 km2
Thickness = 0.006 km
Volume = 0.0048 km3
Step 2d
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1

## Slide 15: Don’t Put Wells Too Close
R
X
W
V
U
T
S
R
X
W
V
U
T
S
2
1
Well A
Well B
We can not drain one cell more than 80%
In this example, cell V2 would have 80% recovery from well B; no additional recovery for well A
However, cells U2 and V3 can contribute 40% to well A and 40% to well B
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1

## Slide 16: Use a 1 Cell Buffer
40%
40%
40%
80%
40%
40%
80%
40%
40%
80%
40%
40%
40%
R
X
W
V
U
T
S
R
X
W
V
U
T
S
2
1
Well A
Well B
Cell V2 is drained:
  40% from well A
  40% from well B

## Slide 17: Total Surface Volume
Gas Expansion factor = 111
Well A:
Subsurface Volume = 0.0147 km3
Surface volume = 0.0147 * 111
Surface volume = 1.63 km3
Well B:
Subsurface Volume = 0.0048 km3
Surface volume = 0.0048 * 111
Surface volume = 0.53 km3
Step 2e
TOTAL Gas Volume:
A + B = 2.16 km3
R
X
W
V
U
T
S
R
X
W
V
U
T
S
2
1
Well A
Well B
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1

## Slide 18: Value of the Gas
We will turn the gas volume into mmBTUs and use a price per 50 cents per mmBTU
Value:
Gas Volume * 36x106
Equals 78x106 mmBTUs
Multiply by $0.75
Equals $58.5 million
Step 3
TOTAL Gas Volume:
A + B = 2.167 km3
R
X
W
V
U
T
S
R
X
W
V
U
T
S
2
1
Well A
Well B
12
6
13
7
10
5
11
8
8
4
8
7
5
1
6
4
2
5
4
1
2
1
1
1

## Slide 19: Total Costs
There are four (4) components of the total cost:
  Exploration = $50 million
  Development = $75 million
  Start-Up (platform and production drilling)
  Operations (for 25 years)

## Slide 20: Start-Up Costs
To determine start-up costs:
  Multiply the number of platforms in your plan by $30 million. [one platform = $30 M]
  If any of the platforms have more than one well, then add $2 million for each additional well on the platform to expand capacity beyond a single well. [two wells so add $2 M]
  Total platform cost [$32 M]
  Multiple the total number of wells by $3 million – the production well drilling costs. [2 wells = $6 M]
  Total start-up costs. [$38 M]
Step 4

## Slide 21: Operation Costs
Operating 1 platform and 2 wells for 9000 days:
  Multiply the number of platforms by $100 million ($4 million /year *25 years). [one platform = $100 M]
  Multiply the number of wells by $2.5 million ($0.1 million/year *25 years). [two wells = $5 M]
  Total operating costs [$105 m]
Step 4

## Slide 22: Total Costs
Exploration = $50 M
Development = $75 M
Start-Up = $38 M
Operations = $105 M
TOTAL = $268 M

## Slide 23: Profit (Loss)
Profit = Value – Costs
For this scenario
  Profit = $58.5 M - $268 M = (-$209.5 M)
This case leads to a BIG loss; we would not propose this development plan!
But we did not drill in an optimum location

## Slide 24: Getting Started
As a team, devise 3 or 4 development plans (N wells from M platforms)
Have each team member ‘run the numbers’ for one of the plans
Compare the profits associated with the different plans
Decide on the plan you would recommend
Prepare a brief report

## Slide 25: Contents of Your Report
The surface location of the platform(s)
The number of wells to be drilled from the platform(s)
The targeted (central) cell for each well
The total gas value in $ million (7-a)
The total costs in $ million (7-b)
The estimated profit in $ million (7-c)

## Slide 26: Exercise 32b
Questions?
Notes: Slide Ex-32b.12