## Slide 1: Petroleum Geology & Geophysics
Production Geoscience
Time
Early in the
Business Cycle
Late in the
Business Cycle
Regional
Compartment-Scale
Reservoir-Scale
Prospect-Scale
Block-Wide
Scales of Analysis
1. Capture
3. Initiate
4. Deplete
2. Discover
Abandon/Sell
Exploration
Development
Production

## Slide 2: An Asset’s Life Cycle
Capture Opportunities
Discover Hydrocarbon
Initiate Production
Deplete the Field
New Ventures
Exploration
Development
Production
Notes: Review – an asset’s life. In this lecture, we will focus on the field production stage

## Slide 3: Changes with Business Stage
Time
Early in the
Business Cycle
Late in the
Business Cycle
Regional
Compartment-Scale
Reservoir-Scale
Prospect-Scale
Block-Wide
Scales of Analysis
1. Capture
3. Initiate
4. Deplete
2. Discover
Abandon/Sell
Geoscience
Production &
Engineering
Information & Effort
Info
Effort
Exploration
Development
Production
Notes: This chart shows how things change over the life of a asset. The scale of the analysis progressively zooms in from regional to individual compartments within a producing field. Geoscience information always increases. Geoscience effort peaks in the early production stage. Information on production and engineering is minimal during exploration; it becomes more and more significant until the field is near abandonment.

## Slide 4: Phase 4
To Maximize Production while Minimizing Costs
Depletion the Field
COMPARTMENT-SCALE
High Resolution Seismic
Res. Compartment Mapping
Detailed Attribute Analysis
Time-Lapse (4D) Seismic
Calibrated Res. Simulation
New Pay Zones
Deeper/Adjacent Targets
PRODUCTS:
Additional Reserves
Optimized Well Locations
Enhanced Recovery Plans
Field Depletion Plans
Maximize Production
Minimize Costs
When to Abandon?
Production G&G
Notes: This slide reviews the analysis and products associated with the field production stage – where we want to deplete the field. We will talk about some of these types of analysis and their products in this lecture, but only scratch the surface.

## Slide 5: Questions in the Production Phase
How should we manage the field so as to maximize our investments?
Can we monitor how oil is being swept out of the reservoir?
What about injection wells and other enhanced recovery methods?
Is there more oil in the vicinity, either at deeper depths or in nearby traps?
Can we build and calibrate a field simulation model so we can test future recovery with different drilling scenarios?
Notes: These are a few of the questions that geoscientists will want to answer during the production phase.

## Slide 6: High Resolution Seismic Data
http://www.geoexpro.com/articles/2013/02/improved-resolution-and-penetration-with-broadband-3d
Once an asset has been discovered and the decision to develop the field has been made, often there is a reason to get better seismic data, either through reprocessing or reacquisition
Exploration Stage Data
Production Stage Data
Notes: The need for great seismic data quality increases as more geologic detail is needed. For example, if I place an injection well at location X, how will it impact production from well #12? Will fluid flow be inhibited by small faults or facies changes?
The data used in exploration and development may not be adequate. We may be able to reprocess the existing data. We may need to acquire higher quality seismic data. The next slide zooms in on the yellow boxes.

## Slide 7: High Resolution Seismic Data
http://www.geoexpro.com/articles/2013/02/improved-resolution-and-penetration-with-broadband-3d
Exploration data versus production-stage data. A fluid contact is not seen in the section on the left but is apparent on the right. The reservoir is blue to orange.
Exploration Stage Data
Production Stage Data
Top
Reservoir
Flat
Spot
Notes: Note the improved seismic data quality on the right. The reflection “bands” are thinner – indicating more high frequency content and better vertical resolution. The “jitter” in the reflections is also reduced. Of importance, a flat spot can be interpreted in the data in the right.

## Slide 8: Select High Resolution 2D Lines
http://csegrecorder.com/articles/view/no-magic-from-5d-interpolation-on-a-coarse-3d-oilsands-dataset-case-history
In some cases, several high resolution lines may be shot to supplement existing 3D data.
Exploration 3D Data
Production 2D Line
Notes: If more seismic data is needed, we may not acquire a full 3D survey. Sometimes we may supplement reprocessed 3D data with high resolution 2D lines.

## Slide 9: Reservoir Compartment Mapping
https://www.researchgate.net/figure/240430676_fig2_Fig-2-Top-Barrow-reservoir-Base-Muderong-depth-structure-map-20-m-contours-Free
Existing, re-processed or re-acquired data is worked in much more detail for the reservoir interval(s)
Each compartment of the field is mapped and the impacts on production evaluated
Depth Structure Map
C. I. = 20 m
Notes: For the production phase, we need as much detail on the reservoir as possible. The reservoir is usually composed of numerous compartments – elements that will have independent fluid movements. We can have vertically segregated compartments – or zones (e.g., upper, middle, lower zones). We can also have horizontally segregated compartments – or fault blocks. The map is a depth structure map of the top of a reservoir showing how the reservoir is broken into numerous fault blocks.

## Slide 10: Detailed Attribute Analysis
0 km 1
Gas
Response
RMS Amplitude Map
over the Reservoir Interval
Notes: Often we can use seismic attributes to map out the extent of HC. Here RMS (root mean square) amplitude is a good indicator of the extent of a gas field. Not every field is this easy to map, but often a combination of attributes can help define the field.

## Slide 11: Time-Lapse Seismic (aka 4D)
3D surveys are acquired after production has started (monitor surveys) and compared to a 3D survey acquired prior to production (the base survey)
Difference between the two are used to monitor fluid movement within the reservoir
1985
Gullfaks Field
http://www.geoexpro.com/articles/2009/05/4d-geophysical-data
1999
Statoil
Notes: There are seismic methods to help us understand how HCs have moved in a field under production. These methods are called by two (2) names: time-lapse seismic or 4D seismic. Two or more 3D high-quality seismic surveys are acquired and processed as similarly as possible. The first survey, before production starts or soon thereafter, is called the base survey. Then other surveys, called monitor surveys, are acquired several years later. The idea is that the only thing that significantly changes is related to the movement of fluids. The two (2) surveys are subtracted to emphasize the differences. Big differences indicate a change in fluid type – HC being flushed and replaced by brine. Small differences signify no or small movement of fluids. If a compartment with HCs shows small differences, an infill well might be drilled to produce HCs that have not been swept. On this slide, two (2) surveys from the Gullfaks field are displayed. The 1985 survey is the base survey. 14 years later a monitor survey was obtained. Note the “yellow” reflector is much less extensive on the 1999 data.

## Slide 12: Time-Lapse Seismic (aka 4D)
For this North Sea field, time lapse seismic was used to monitor oil saturation from 1985 to 2005
The disappearance of the hot colors (high oil saturation) demonstrates how oil has been swept out of the reservoir
Oil Saturation
HIGH
LOW
1996
1999
2003
2005
1985
http://www.geoexpro.com/articles/2009/05/4d-geophysical-data
Notes: Here is another display of Gullfaks data. Here seismic attributes have been related to HC presence. Note how the extent of the hot colors dwindles from 1985 through 2005. Such information is of great value to production geoscientists and engineers.

## Slide 13: Calibrated Reservoir Simulation
We want to predict future oil and gas production given existing wells plus new wells (producers and injectors)
To do this, we build a computer model of the field
We assign each cell in the model with rock, fluid and physical properties (e.g., porosity, temperature)
We model past production and adjust the parameters until they match the known (historical) production
http://www.beicip.com/integrated-field-studies
Then we can use this calibrated model to predict future production
Notes: One thing commonly done for larger fields is to build a 3D model of the field in the computer. Each cell in the model is assigned rock, fluid and physical properties (temp, pressure). Then the software models how fluids would move given current and future wells (producers and injectors).
The first phase of modeling is to match production to from its start up to the current time. Matching known production is how the model parameters are calibrated. There are static (constant over time) properties, such as rock types. There are also dynamic (time-varying) properties, such as oil saturation. Phase one is done when a reasonable history match is obtained.
The second phase of modeling is to predict future production. Like a weather forecast that shows how the weather will proceed for the next several hours. This can be done with the existing wells. More importantly, it can predict future production if new production or injection wells are drilled. In this way, we can test if drilling new wells in specific locations will boost oil and gas recovery enough to make a profit.

## Slide 14: A Geologic Model
An integration of all geologic, geophysical, petrophysical and interpreted or conceptual information about a reservoir into a single 3D numerical description of that reservoir
Structural Interpretation
Stratigraphic Interpretation
Petrophysical Interpretation
Geophysical Interpretation
Notes: The subsurface (geologic model) is an integration of all geologic, geophysical, petrophysical and interpreted or conceptual information about the reservoir into a single 3D numerical description of your reservoir.

## Slide 15: A Geologic Model
Each cell can be populated with rock & fluid properties:
  Facies
  Porosity
  Permeability
  Temperature
  Fluid Saturation
  Etc.
1m
75 m
Perm
250 mD
Sand
Shale
Perm
0.1 mD
50 m
Notes: Each cell in the model is assigned rock fluid and physical properties: Rock type (lithology); Porosity; Permeability; Temperature; Fluid Saturation; Water properties; Oil properties; Gas properties
Cell size can vary depending on the field size, computing resources, etc., but they are typically about 50 to 100 m in X and Y and about 1 m in depth (Z).

## Slide 16: Reservoir Simulation
Geologic Model
Reservoir Simulation
INPUT
FEEDBACK
Oil Production
Production
Time
HISTORY
MATCH
Actual in Blue
Modeled in Red
Notes: A reservoir simulation (computer model of flow within the geologic model) is a very useful tool for production people. The first step is the building of a detailed geologic model of the reservoir (as just described).
Then fluids are populated within each cell of the geologic model along with fluid properties. The reservoir simulator models how the fluids move through time. Until recently, the first simulation would be run after about 5 years of production time. The simulation would be calibrated by doing a history match - comparing the simulated production (red curve) with the actual production data (blue boxes). If a reasonably good history match is obtained, the model is taken to be fairly accurate. Then, we can simulate future production – 10, 20, 30 years into the future:
  We can do some ‘what if’ scenarios – e.g., if we placed three (3) additional producers at these locations and five (5) injectors at these locations, how much additional oil would we produce?
  If the cost of these eight (8) wells is less than the value of the additional oil, we might do it.
  Obviously if the cost of the eight (8) additional wells would not be recovered, we would not do it – look for other ‘profitable’ scenarios.
  We can also look for portions of the reservoir that, according to the simulation, are not swept of oil and target these locations with additional wells – if profitable.

## Slide 17: Let’s Fast Forward a Number of Years
The Alpha field has been producing for 5 years
We want to maximize production
Build a
Geologic
Model
Develop a
Reservoir
Simulation
Can We
Match Past
Production?
Model
Future
Production
Iterate to Match
Production History
YES
NO
Notes: Let’s go forward 5 years after the start of production (drawing fluids out of the reservoir). Our main objective is to maximize production while minimizing the costs. We would build a computer model of the subsurface – with rocks and fluids. We would simulate how each well should have produce fluids over the last 5 years of production. We use the actual well production history to calibrate the model (simulation).
If we get the model to match actual production, we build confidence that the model is close to reality. Then we can model production into the future, e.g., the next 10 years. With the model, we can test ideas such as “what if we add to producers at locations A, B and C and an injector at location Z?”

## Slide 18: Using a Simulation
How do we use this information?
Field development planning
Field production optimization
Reservoir surveillance
Past Production
Future Production
Past Time (yrs)
Oil Rate
Future Time (yrs)
Oil Rate
Base Case
EOR
Infill Drilling
Actual
Modeled
Present Day
Present Day
Notes: To summarize, the first task is to get a history match – a model (simulation) that matches the history of field production. If this is done, then we start to model future production.
We can see the impact of using EOR – enhanced oil recovery methods
Or of doing infill drilling
The main question is will the cost of EOR and/or infill drilling going to result in enough extra production that the extra costs are more than recovered by the extra oil or gas to sell

## Slide 19: Lecture 33
Questions?