## Slide 1: Exercise 33a
A1 Gas
Sand
Mapping the A-1 Gas Sand
Mapping a Gas Sand
Your Task:
  Use the diagnostic amplitude response to map the extent of the A-1 sand where it is filled with gas.
Notes: Title slide with main task.

## Slide 2: Exercise 33a
Background
2
A well was drilled in 1972 to produce gas from a deep reservoir interval. While drilling, a 12 m gas sand was encountered. At this time, they were not able to evaluate the extent of the gas sand or how much gas could be recovered. So the A-1 sand was not completed (set up to be produced).
In 1999, a 3D seismic survey was acquired to help production geoscientists with managing the deeper field. The presence of gas in the A-1 sand gives it an anomalously strong seismic amplitude. This enabled seismic interpreters to map the areal extent of the A-1 gas.
In exercise 1a, you will start to map the extent of gas in the A-1 sand. The seismic response (impedance contrast) between shale and the gas-charged A-1 sands is significantly greater than the seismic response between shale and the water-filled A-1 sands or silts. The diagnostic large negative seismic amplitude indicates the extent of the A-1 gas.
Notes: This slide gives the background for the task given in this exercise.

## Slide 3: Study Area
Study Area
Well
2 km
Time Structure
Top of A-1 Sand
Notes: This is a more regional map of the study area. The red box is where you will focus. Note the well location. Also note the fault (brown) that is an extensional fault, down to the southwest.

## Slide 4: A Shallow Gas Discovery
Self Potential
(millivolts)
Resistivity
(ohm-meters)
50 100
.2 1000
Depth
Feet
A-1 Gas
Sand
40 ft
12 m
Notes: Here is a portion of the self potential (SP) and Resistivity logs from the well. There is a 40 ft (12 m) thick sand, which is called the A-1 sand. Note the log pattern indicates a fining upward sand, the classic signature of a fluvial sand. The resistivity log indicates this sand has gas in its pore space.

## Slide 5: A-1 Sand Study Area
820
900
860
840
800
880
480
460
500
440
420
1 km
Well
Notes: Here is the base map for the study area. The seismic lines are from a 3D survey. East-west lines are in the 800 range. North-south lines are in the 400 range. The brown lines indicate faults. The lines that are bolder have already been interpreted for you.

## Slide 6: Inline 840 and Well Synthetic
A1 Gas
Sand
Notes: This is line 840 (west to east). The depth of the A-1 sand is indicated. Note how there is a very large amplitude response. The high amplitudes are due to the presence of gas in the A-1 sands. Thus we can use strong seismic amplitudes as a means to map the extent of the gas-filled sands.

## Slide 7: Amplitude Signature of the Gas Sand
A1 Gas
Sand
Extent of Gas
Notes: With paper displays, there is an option to “clip” the amplitudes. Very large positive or very negative numbers are not fully drawn to prevent over-plotting of traces. Note in the red box how in the white cycle the individual traces are squared off (clipped). These displays have been set so clipping occurs when the amplitudes are indicative of the presence of gas. Note in the cyan box the traces in the white cycle are rounded (not clipped). This indicates the sands have brine (salt water) in the pores. We can use the clipped traces to get an estimate of the extent of the gas-filled sand.

## Slide 8: Mapping Approach – Step 1
Use a color pencil (or highlighter) to mark JUST where the A-1 amplitude is anomalously low, where the trough is ‘clipped’ (i.e., squared off)
Notes: The process for you is to tie the A-1 horizon, perhaps with a thin pastel line. Then mark with a deeper and wider color line where the traces appeared to be clipped. Mark the extent of the clipped traces (gas present) on the basemap.

## Slide 9: Mapping Approach – Step 2
820
900
860
840
800
880
480
460
500
440
Well
420
520
Mark on the base map the extent of the anomalously low amplitudes on line 840
Note that intersecting lines 460, 480, 500 should also have anomalously low amplitudes
Notes: Here the extent of gas along line 840 is marked. Three of the north-south lines intersect 840 where the amplitudes are anomalously strong.

## Slide 10: Mapping Approach – Step 3
Tie the A-1 sand from an interpreted line (840) to an uninterpreted line (e.g., 480)
Fold line 840 where it intersects line 480
Position line 840 on line 480 at the intersection point
transfer the A-1 horizon from line 840 to line 480
440
420
460
500
520
540
W
E
Inline 840
800
780
840
820
860
900
880
N
Crossline 480
S
440
420
460
480
W
Inline 840
Notes: This illustrates how the interpretation on line 840 is “tied” to line 480.

## Slide 11: Mapping Approach – Step 3
820
900
860
840
800
880
480
460
500
440
Well
420
520
Mark on the base map the extent of the anomalously low amplitudes on line 480
Note that intersecting lines 820, 860, 880 should also have anomalously low amplitudes
Notes: Now we can mark the extent of the strong negative response on line 480.

## Slide 12: Mapping Approach – Steps 4, 5, …
820
900
860
840
800
880
480
460
500
440
420
520
Continue to map the A-1 sand trough where it has anomalously low amplitude by tying uninterpreted lines to interpreted lines until you are done
Well
Notes: You will mark the extent of gas on several lines. Then you can draw a polygon to define the extent of the gas field. NOTE: The polygon shown here is NOT correct, just to illustrate the process.

## Slide 13: Your Lines
820
900
860
840
800
880
480
460
500
440
420
1 km
Well
Notes: Map of the study area showing faults and line locations. The solid red lines have been interpreted for you.

## Slide 14: Exercise 33a
Questions?