## Slide 1: Exercise 33b
Recoverable Gas from the A-1 Sand
Volume of Recoverable
Gas
Your Task:
  Use an amplitude map for the A-1 sand to get the field’s area and then the volume of recoverable gas at the surface.

## Slide 2: Exercise 33b
Introduction
2
In Exercise 33a, you mapped the extent of the gas-filled A-1 sand with 11 lines. Now you will use a map based on all the 3D seismic data showing the amplitude at the top of the A-1 sand.
First you will estimate the area of this gas field. Then you will use data, mainly from the logs from the original well, to estimate the volume of gas that could be recovered from this reservoir interval.
The recoverable gas volume and a prediction of future gas prices gives us a value for the A-1 reservoir interval in dollars.
Notes: Gives the objective – to get the volume of gas we hope to get to the surface and sell. The value of the gas we sell minus all the costs indicates how much profit our company makes, if any.

## Slide 3: Well Logs Give Important Parameters
Self Potential
(millivolts)
Resistivity
(ohm-meters)
50 100
.2 1000
Depth
Feet
A-1 Gas
Sand
40 ft
12 m
Notes: This shows part of two (2) logs from the original well – the self-potential (SP) log on the left and the resistivity log on the right. SP is used to interpret sand content; the 12 m thick A-1 sand is colored yellow. Resistivity is used to detect HCs; the red indicates gas in the A-1 at this location.

## Slide 4: A-1 Sand Anomalous Amp. - Manuel
820
900
860
840
800
880
480
460
500
440
Well
420
1 km
Notes: This is the way I enclose the high amplitudes that I mapped. To the ENE is a fluvial system that broadened, perhaps into a splay. The fault (brown) is down to the west and forms the SW boundary of the field.

## Slide 5: A-1 Sand Anomalous Amplitude
Gas
Response
1 km
Notes: Here is what can be done with a 3D survey and seismic interpretation software. The top reservoir was mapped throughout most of the larger area. Then, the amplitudes along this horizon were displayed. The range of amplitudes and color bar were adjusted so that areas with gas (known or interpreted) shown as orange-to-red. There is more detail for this area then one can get from several seismic lines. Now the splay to the west is more obvious.

## Slide 6: A-1 Sand Anomalous Amplitude
Gas
Response
1 km
Each square
200x200 m
Notes: The amplitude map from the previous slide has been superimposed by a square grid. Each red box is 200 m by 200 m. We can use this grid to get an estimate of the area of the field.

## Slide 7: A-1 Sand Anomalous Amplitude
Gas
Response
1 km
Each square
200x200 m
Notes: Now the image has been changed into black and white.

## Slide 8: A-1 Sand Anomalous Amplitude
Each square
200x200 m
Notes: This is a zoomed in image of the last slide. I used this image to draw a polygon around the high amplitudes, to approximate the extent of the field.

## Slide 9: A-1 Sand Anomalous Amplitude
L
M
N
O
A
B
C
D
E
F
G
H
I
J
K
Totals
1
1
2
4
1
4
2
2
13
2
4
4
4
2
16
Each square
200x200 m
Each unit
100x100 m
Notes: This is the figure you get in the exercise. Note columns “A” through “O.” I estimated to the nearest ¼ how many cells are within the polygon for columns A, B and C. The total for each column (in ¼ cells = 100m x 100m) is written near the bottom. You will be asked to total all the other columns.

## Slide 10: Recoverable HC - Overview
Our ultimate goal is to know how much HC is in the reservoir and what portion we can produce, the estimated ultimate recovery (EUR)
Our initial focus is on the amount of HC in-place
It is beyond the scope of this course to estimate the portion that can be produced (typically about 15 to 45% for oil; can be higher for gas)
So how do we get HC In-Place?
Notes: I’ll now review how we get:
- the volume of gas in-place; in the reservoir rocks at reservoir conditions, and then
- the volume of gas we expect to get to the surface at surface temperatures and pressures

## Slide 11: Obtaining HC In-Place
We start by estimating the total volume of rock
Then we reduce the volume step-by-step until we get an estimate of the volume of HC in the reservoir – gas in the case of Barracouta
Total Rock
Volume
Res Sand
Volume
Non-Res
Non-Net
Non-Res
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
RESERVOIR
Notes: This summarizes the process to get the gas in-place. The next several slides gives more details.
- Get the total rock volume,
- Get the reservoir sand volume,
- Get the net pore volume,
- Get the HC volume at reservoir conditions

## Slide 12: Total Rock Volume
A first approximation:
  Map the areal extent of the trap (planimeter)
  Estimate how far down dip the HCs extend
  Convert the isochron map (ms) to an isochore map (m or ft) using velocity data from the well
  Combine the HC extent and the thickness to get a total rock volume (km3 or acre/ft)
Total Rock
Volume
Field Area
*
Aver. Thickness
Total Rock Vol.
Notes: To get the total rock volume:
- we get the area of the field
- we get an average thickness for the reservoir interval
- area times thickness equals volume

## Slide 13: Reservoir Rock Volume
A first approximation:
  Start with the total rock volume
  Estimate the net-to-gross for the reservoir interval (good sands versus waste rock)
  Net-to-gross often varies by the environments of deposition
  For our field:
    N/G = 75%
Res Sand
Volume
Non-Res
Non-Net
Non-Res
Total Rx Vol.
*
Net-to-Gross
Res. Rock Vol.
Notes: To get the reservoir rock volume:
- start with the total rock volume,
- estimate the net (reservoir) percent of the total, e.g., 75% of the total is good reservoir sand.

## Slide 14: Pore Volume
A first approximation:
  Start with the reservoir sand volume
  Use a porosity value (percentage of volume that represents the pore space)
  Porosity often varies by the environments of deposition
  For our field:
    Φ = 17%
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Res. Sand Vol.
*
Porosity
Pore Volume
Notes: To get the pore volume:
- we start with the reservoir volume’
- we get a porosity value, (e.g., 17%)
- we multiply the two numbers.
This is an estimate of the volume between sediment grains, where fluids can be.

## Slide 15: Hydrocarbon Volume
A first approximation:
  Start with the net pore volume
  Use a HC saturation value (e.g. 80% HC saturation means 80% of the pore space contains HCs, the other 20% has irreducible water)
  For this field, we will assume a HC saturation of 90%
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
Net Pore Vol.
*
HC Saturation
HC Volume
Notes: Finally, we can get in-place hydrocarbon (HC) volume by using a value for HC saturation, e.g., 90%. This means 90% of the pore space has gas; 10% has water/brine. Net pore volume times HC saturation = in-place HC volume.

## Slide 16: Recoverable HC
We need a recovery efficiency to go from HC in-place to recoverable HC
We will assume a 50% recovery efficiency
Many factors go into the recovery efficiency, in particular, how effective the reservoir’s “plumbing” is, which is related to permeability
There is also a volumetric expansion due to the drop in Temperature & Pressure
In-Place HC
*
Expan. Factor
*
Recovery Eff.
Recoverable V.
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
In-Place
at Depth
Recovered
at Surface
Gas
Expansion
Notes: We are more interested in the volume of gas we can get to the surface – and sell to make money. There are two (2) factors:
- the recovery efficiency, e.g., 50%
- the gas volume expansion as it comes up to the surface and cools and depressurizes.

## Slide 17: Procedure
Step 1 | Get the Area in "blocks"
Step 2 | Get the Area in km2
Step 3 | Enter the Average Thickness
Step 4 | Multiply N/G by Porosity
Step 5 | Multiply by HC Saturation
Step 6 | Get the Gas Volume at Reservoir Conditions
Step 7 | Assume a Recovery Efficiency
Step 8 | Get a Gas Volume at Surface Conditions
Step 9 | Convert from m3 to ft3
Notes: This is the calculation sheet that you have and will fill out as you do the exercise.

## Slide 18: Exercise 33b
Questions?
Notes: Slide Ex-33b.18