## Slide 1: Exercise 33b: Recoverable Gas from A-1
Volume of Recoverable
Gas
Your Task:
  Use an amplitude map for the A-1 sand to get the field’s area and then volume of recoverable gas.
Notes: Slide SOLU Ex-33b.1
A review of exercise 33b.

## Slide 2: A-1 Sand Anomalous Amplitude
Each square
200x200 m
L
M
N
O
A
B
C
D
E
F
G
H
I
J
K
Totals
1
1
2
4
1
4
2
2
13
2
4
4
4
2
16
Notes: This is what was shown during the exercise introduction. Columns A, B and C have totals of 2, 13 and 16 units of 100x100 m.

## Slide 3: A-1 Sand Anomalous Amplitude
Each square
200x200 m
15
3
23
23
14
12
15
20
22
16
23
2
13
16
21
L
M
N
O
A
B
C
D
E
F
G
H
I
J
K
TOTAL
238 units
(100x100 m)
Notes: This shows the total that I came up with – 238 units (not cells).

## Slide 4: Getting the Area
1 Cell = 200x200 m
1 Unit = 100x100 m = 0.1x0.1 km
238 units = 238 x 0.01 = 2.38 km2
Notes: This works out to be an estimate of 2.38 square kilometers.

## Slide 5: Computations
ROW | PARAMETER | VALUE | UNITS
1 | Area in Square kilometers | 2.38 | KM3
2 | Gross Thickness in kilometers | 0.01 | 0
3 | N:G * Porosity | 0.1275 | - - -
4 | HC Saturation | 0.9 | %
5 | HC Pore Volume in cubic kilometers | 0.00273105 | KM3
6 | Recovery Efficiency | 0.5 | %
7 | Recoverable Gas Reservoir Conditions in cu. Km | 0.001365525 | KM3
8 | Recoverable Gas at Surface in Billon cubic meters | 0.099683325 | Billion M3
9 | Recoverable Gas at Surface in Bcf | 3.518821373 | Billion Ft3 (BCF)
TOTAL GAS
3.5 BCF
Notes: Here is the computation sheet with my numbers filled in. I get 3.5 billion cubic feet of gas at the surface.

## Slide 6: A-1 Sand Time Structure from the WSW
N
Well
Fault
Notes: 8
Here is a display of a perspective view of the top of the A-1 sand for the entire 3D survey area. The view is from the west-southwest. The well you have been using is marked. You can see the down to the southwest fault that limits the field. The dotted red polygon is the field outline we have been defining and sizing.
R
Tip bounded fault is about 3.5 miles long (~20,000 ft). 200 ms of throw translates to about 800 ft (8000 ft/s) to 1000 ft (10,000 ft/s) of throw or structural relief. Length/throw is 20000/1000 = 20:1

## Slide 7: Exercise 33b
Questions?