## Slide 1: Bayesian inversion and Bayesloc Multiple-Event Location
Performance Measures x.x, x.x, and x.x
Stephen C. Myers
LLNL Ground-based Nuclear Detonation Detection (GNDD)

## Slide 2
Bayes Theorem
Joint Model (m) and Data (d) Domain
P(m)
P(d)
P(m,d)
We want to find the joint probability of the model (m) and the data (d)
Joint probability recast as conditional probability, model if data
Conditional probability can also be recast as data if model
The conditional probabilities are equal
Rearranging results in the common expression of Bayes Theorem
Let’s say P(m) and P(d) are constant in a defined area
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 3
Grid-search Bayesian Inversion
Model (m) and Data (d) domain
P(m)
P(d)
P(m,d)
We want to find the joint probability of the model (m) and the data (d)
Joint probability recast as conditional probability (model if data)
Conditional probability can also be recast as data if model
The conditional probabilities are equal
Rearranging results in the common expression of Bayes Theorem
We could grid the space and compute the probability
Point 1)
1
2
Point 2)
Point 3)
3
It is easy to see that P(m|d) = 1/C for each point where P(m) and P(d) overlap
C is a normalizing constant =P(d)=
Sum(P(d|m)P(m))
Notes: For non-linear cases an inversions involving many model parameters there is a 3rd option…

## Slide 4
Grid-search Bayesian Inversion
Model (m) and Data (d) domain
P(m)
P(d)
P(m,d)
We want to find the joint probability of the model (m) and the data (d)
Joint probability recast as conditional probability (model if data)
Conditional probability can also be recast as data if model
The conditional probabilities are equal
Rearranging results in the common expression of Bayes Theorem
We could grid the space and compute the probability
Point 1)
1
2
Point 2)
Point 3)
3
It is easy to see that P(m|d) = 1/C for each point where P(m) and P(d) overlap
C is a normalizing constant =P(d)=
Sum(P(d|m)P(m))
Grid search is an exhaustive approach.
It can be computationally prohibitive.
Notes: For non-linear cases an inversions involving many model parameters there is a 3rd option…

## Slide 5
Bayesian inversion through sampling
Draw samples from the probability density function then infer the solution based on sample density: maximum likelihood point and uncertainty.
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 6
Bayesian inversion through sampling
Advantages:
Explore large model space with fewer samples
Model space can be highly nonlinear and multi-modal
Draw samples from the probability density function then infer the solution based on sample density: maximum likelihood point and uncertainty.
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 7
Bayesian inversion through sampling
But how do you draw samples from a distribution you don’t know?
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 8
Let’s start with what we can do:
We can evaluate the ratio of data probability (~data fit) for two sets of model parameters (). As it turns out, this ratio is all we need to know.
Bayesian inversion through sampling
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 9
Let’s start with what we can do:
We can evaluate the ratio of data probability (~data fit) for two sets of model parameters (). As it turns out, this ratio is all we need to know.
∫ℝ (m,A)P(m)dm->∫ℝp(x,A)π(x)dx=∫ℝd[∫Ap(x,y)1(x∉dy)dy+r(x)1(x∈dy)]π(x)dx=∫ℝd[∫Ap(x,y)1(x∉dy)dy]π(x)dx+∫ℝdr(x)1(x∈A)π(x)dx= ∫ℝd[∫Ap(x,y)1(x∉dy)dy]π(x)dx+
∫Ar(x)π(x)dx=∫A[∫ℝdp(x,y)π(y)dx]1(x∉dy)dy+∫Ar(x)π(x)dx=⋆∫A[∫ℝdp(y,x)π(x)dx]1(x∉dy)dy+∫Ar(x)π(x)dx=∫A(1−r(y))π(y)dy+∫Ar(x)π(x)dx
=∫AP(m)dx.
Proof from Chib and Greenberg, Understanding the Metropolis-Hastings Algorithm, The American Statistician, 1995
If we have a target distribution of model parameters (P(m) in this case) and we have a distribution that prescribes the probability of transitioning from one set of model parameters to a new set of parameters ((m,A)) within a subdomain A, then …
Bayesian inversion through sampling: Markov-Chain Monte Carlo
Proof (sorry about the change in notation)
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 10
Let’s start with what we can do:
We can evaluate the ratio of data probability (~data fit) for two sets of model parameters (). As it turns out, this ratio is all we need to know.
∫ℝ (m,A)P(m)dx->∫ℝp(x,A)π(x)dx=∫ℝd[∫Ap(x,y)1(x∉dy)dy+r(x)1(x∈dy)]π(x)dx=∫ℝd[∫Ap(x,y)1(x∉dy)dy]π(x)dx+∫ℝdr(x)1(x∈A)π(x)dx= ∫ℝd[∫Ap(x,y)1(x∉dy)dy]π(x)dx+
∫Ar(x)π(x)dx=∫A[∫ℝdp(x,y)π(y)dx]1(x∉dy)dy+∫Ar(x)π(x)dx=⋆∫A[∫ℝdp(y,x)π(x)dx]1(x∉dy)dy+∫Ar(x)π(x)dx=∫A(1−r(y))π(y)dy+∫Ar(x)π(x)dx
=∫AP(m)dx.
Proof from Chib and Greenberg, Understanding the Metropolis-Hastings Algorithm, The American Statistician, 1995
This step requires that the proposal meets the detailed balance condition
P(mi) (mi,mi+1)=P(mi+1)(mi+1, mi)
If we have a target distribution of model parameters (P(m) in this case) and we have a distribution that prescribes the probability of transitioning from one set of model parameters to a new set of parameters ((m,A)) within a subdomain A, then …
Bayesian inversion through sampling: Markov-Chain Monte Carlo
Proof (sorry about the change in notation)
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 11
Let’s start with what we can do:
We can evaluate the ratio of data probability (~data fit) for two sets of model parameters (). As it turns out, this ratio is all we need to know.
What does this say?
If we conditionally sample P(m|d) with a model parameter transition kernel that satisfies the detailed balance condition, then the resulting Markov Chain will sample the stationary distribution of P(m|d).
∫ℝ (m,A)P(m)dx->∫ℝp(x,A)π(x)dx=∫ℝd[∫Ap(x,y)1(x∉dy)dy+r(x)1(x∈dy)]π(x)dx=∫ℝd[∫Ap(x,y)1(x∉dy)dy]π(x)dx+∫ℝdr(x)1(x∈A)π(x)dx= ∫ℝd[∫Ap(x,y)1(x∉dy)dy]π(x)dx+
∫Ar(x)π(x)dx=∫A[∫ℝdp(x,y)π(y)dx]1(x∉dy)dy+∫Ar(x)π(x)dx=⋆∫A[∫ℝdp(y,x)π(x)dx]1(x∉dy)dy+∫Ar(x)π(x)dx=∫A(1−r(y))π(y)dy+∫Ar(x)π(x)dx
=∫AP(m)dx.
Proof from Chib and Greenberg, Understanding the Metropolis-Hastings Algorithm, The American Statistician, 1995
This step requires that the proposal meets the detailed balance condition
P(mi) (mi,mi+1)=P(mi+1)(mi+1, mi)
If we have a target distribution of model parameters (P(m) in this case) and we have a distribution that prescribes the probability of transitioning from one set of model parameters to a new set of parameters ((m,A)) within a subdomain A, then …
Bayesian inversion through sampling: Markov-Chain Monte Carlo
Proof (sorry about the change in notation)
Notes: See https://www.probabilisitcworld.com/anatomy-bayes-theorem

## Slide 12
There are several commonly used transition kernels: Metropolis-Hastings
Metropolis-Hastings
Transition probability (proposing a new point)
Compute acceptance ratio
Generate u~ Uniform([0,1])
q is a proposal distribution. Often a “random walk” (Gaussian).
If q is symmetric (e.g. Gaussian), the q terms cancel
Evaluate using Bayes Theorem
The P(d) terms cancel!
If a 1, m’ is always accepted
Otherwise, accept based on the ratio of probability of the proposed and current model parameters

## Slide 13
Metropolis-Hastings: Step through a proposal
=
=
P(m)
mi
mi+1
P(mi)
P(mi+1)
u~ Uniform([0,1])
Transition kernel (t)
Recall the proposal procedure
Example

## Slide 14
Probability of the proposal is higher so accept it
=
=
P(m)
mi
mi+1
P(mi)
P(mi+1)
u~ Uniform([0,1])
Transition kernel (t)
For our example
=1
Recall the proposal procedure
Example

## Slide 15
What if we reversed the proposal?
=
=
P(m)
mi
mi+1
P(mi)
P(mi+1)
u~ Uniform([0,1])
Transition kernel (t)
For our example
=1
So
Recall the proposal procedure
Example
This is the reversed proposal proposition

## Slide 16
Metropolis-Hastings sampling satisfies the detailed balance condition
=
=
P(m)
mi
mi+1
P(mi)
P(mi+1)
u~ Uniform([0,1])
Transition kernel (t)
For our example
=1
So
Metropolis-Hastings meets the detailed balance condition, by design
Recall the proposal procedure
Example
This is the reversed proposal proposition

## Slide 17
MCMC with our cartoon inversion
Model (m) and Data (d) domain
P(m)
P(d)
P(m,d)
Markov-Chain Monte Carlo
Start at some point m0
Propose a new point in model space
  If the new point is higher probability accept it, becomes m0+1
  If new point is lower probability, accept it a ratio proportional to the probability of the current and proposed state, selected point becomes new state m0+1
Repeat until samples adequately characterize P(m|d).
Density of accepted points infers P(m|d)
start
Reject 1
Reject 2
Accept 3

## Slide 18
P(m|d)
mi
mi+1
P(mi)
P(mi+1)
The power of Metropolis-Hastings is that we don’t need to know the analytical form of P(m|d). We only need to evaluate it, P(m|d)=P(d|m)P(m)
Metropolis-Hastings: Advantage

## Slide 19
P(m|d)
mi
mi+1
P(mi)
P(mi+1)
The power of Metropolis-Hastings is that we don’t need to know the analytical form of P(m|d). We only need to evaluate it, P(m|d)=P(d|m)P(m)
The disadvantage is that the M-H can be inefficient if the proposal is poorly tuned.
P(m|d)
mi
mi+1
P(mi)
P(mi+1)
What if the proposal step is too large?
New proposals will tend to be on the tails of the distribution and, therefore, rejected. Many more iterations are needed…
Metropolis-Hastings: Disadvantage

## Slide 20
The disadvantage is that the M-H can be inefficient if the proposal is poorly tuned.
P(m|d)
mi
mi+1
P(mi)
P(mi+1)
What if the proposal step is too large?
New proposals will tend to be on the tails of the distribution and, therefore, rejected. Many more iterations are needed…
Metropolis-Hastings: Disadvantage
Example of inefficient sampling

## Slide 21
P(m|d)
mi
mi+1
P(mi)
P(mi+1)
The power of Metropolis-Hastings is that we don’t need to know the analytical form of P(m|d). We only need to evaluate it, P(m|d)=P(d|m)P(m)
If we know the analytical form of P(m|d), we can sample it directly for each step of the MCMC iteration.
P(m|d)
m

## Slide 22
Gibbs sampling
If the probability of one parameter conditional on all others takes an analytical form, then sample (update) one model parameter at a time, while holding the others constant.
  Geman and Geman, 1984 showed that as i-> , the density of samples represents the joint distribution and the density of samples for each model parameter represent the marginal distribution of each model parameter.

## Slide 23
Gibbs sampling
If the probability of one parameter conditional on all others takes an analytical form, then sample (update) one model parameter at a time, while holding the others constant.
  Geman and Geman, 1984 showed that as i-> , the density of samples represents the joint distribution and the density of samples for each model parameter represent the marginal distribution of each model parameter.
A common Gibbs statistical model (and the one used in Bayesloc) is that
mj~Gau(uj,tj), each model parameter (could be a model parameter subset) is Gaussian
u~Gau(0,w), the means of the set of model parameters are distributed Gaussian
t~Gamma(a,b), the variances of the set of model parameters are distributed Gamma
If these conditions are met,
Then =Gaussian(, )
and =Gamma()
These relationships are derived in textbooks and at https://bookdown.org/rdpeng/advstatcomp/gibbs-sampler.html
Then we just draw a random sample for and , ) to get

## Slide 24
Gibbs sampling
If the probability of one parameter conditional on all others takes an analytical form, then sample (update) one model parameter at a time, while holding the others constant.
  Geman and Geman, 1984 showed that as i-> , the density of samples represents the joint distribution and the density of samples for each model parameter represent the marginal distribution of each model parameter.
A common Gibbs statistical model (and the one used in Bayesloc) is that
mj~Gau(uj,tj), each model parameter (could be a model parameter subset) is Gaussian
u~Gau(0,w), the means of the set of model parameters are distributed Gaussian
t~Gamma(a,b), the variances of the set of model parameters are distributed Gamma
If these conditions are met,
Then =Gaussian(, )
and =Gamma()
These relationships are derived in textbooks and at https://bookdown.org/rdpeng/advstatcomp/gibbs-sampler.html
Then we just draw a random sample for and , ) to get
Gibbs sampling is efficient because the sample is always accepted.

## Slide 25
Let’s apply MCMC to event location
The goal is to find the location and time that minimizes the difference between observed and predicted arrivals
Notes: Our goal is to find the 3d location and the time of an event that minimizes the difference between observed and predicted arrival times.

## Slide 26
Bayesloc models the multiple-event system
Event locations and origin times
Travel time predictions
  Regional travel time bias
  Path specific error
Arrival time measurements (precision)
Arrival time phase assignment
Modeling the whole system enables accurate error characterization

## Slide 27
Bayesloc: conditional probability
We have arrival times for various phases.
We would like to know:
  Event locations.
  Travel times.
  Measurement precision and phase labels.
Statistical model
o = origin time
x = location
T = phase travel times
W = phase labels
s = measurement precision
= travel time error
a = observed arrival times
w = input phase labels

## Slide 28
Bayesloc: Bayesian formulation
Bayesloc probability model
Arrivals conditional on a hypothesized set of event locations
=
Travel time prediction conditional on model and corrections
Phase labels conditional on input labels
Hypocenter priors
Measurement precision and travel time correction priors
Parameters
conditional on data
Bayesian formulation recasts the conditional probability into a collection of forward calculations.

## Slide 29
Bayesloc: measurement uncertainty model
Error decomposition
• Precision (1/Variance)
• (W) phase
• (j) event
• (i) station

## Slide 30
s = 0.75s
Phase(w)
30
Bayesloc: measurement uncertainty model
Error decomposition
• Precision (1/Variance)
• (W) phase
• (j) event
• (i) station
Example probability density
Datum (ijw)
Event (j)
Station (i)
=
Product of precisions down weights components with large variance.
s = 0.6s
s = 1.0s
s = 5.0s
*
*

## Slide 31
Bayesloc: travel-time model
Travel time decomposition
• (M) model prediction
• (a, b) travel-time curve adjustments
• (g) station (i), station-phase (iW), and event (j) adjustments allow for path-specific corrections.
Constraining the station- and event-specific corrections to have mean=0, enables resolution of absolute location.

## Slide 32: Bayesloc Forward Problems: Phase Labels
o = origin times
x = locations
T = phase travel times
W = phase labels
= measurement precisions (pick)
V = measurement precisions (diff)
τ = travel time corrections
a = arrival times (picks)
d = differential arrival times
w = input phase labels
Probability of phase labels given a set of observed arrival times, locations, phase labels, travel time predictions and measurement uncertainties

## Slide 33: Bayesloc Forward Problems: Prior Constraints
o = origin times
x = locations
T = phase travel times
W = phase labels
= measurement precisions (pick)
V = measurement precisions (diff)
τ = travel time corrections
a = arrival times (picks)
d = differential arrival times
w = input phase labels
Input prior probabilities.
Mine event
Pick uncertainty prior
Travel time
prediction prior

## Slide 34: Progressive Sampling of Bayesloc Parameters
Locations
(Metropolis-Hastings)
Origin Times
(Gibbs)
Travel Time Corrections
(Gibbs)
Measurement error
(Gibbs+Slice)
Phase labels
(Gibbs)
First ~200 iterations Only sample event locations
~200 to ~300 Add sampling of measurement precision and phase labels
~400 to N Add sampling of travel time corrections
Different sampling methods are used for efficiency

## Slide 35
Bayesloc: Markov-Chain Monte Carlo
Movie shows the sampling of event locations.
0) Start
1) Burn in
2) sample
Phase residuals for each MCMC step are shown to the right

## Slide 36: Analysis of MCMC samples: Option 1 (preferred)
Compute point density (heat plot)
Contour point density
The area inside a contour can be assigned a probability level

## Slide 37: Analysis of MCMC samples: Option 2
Assume Gaussian distribution
Computer sample mean (e.g. epicenter)
Computer ellipse/ellipsoid using sample covariance
Note that correlation/covariance of all Bayesloc parameters can be examined in a similar fashion.
3D samples
Ellipsoid
Longitude
Latitude
Depth (km)

## Slide 38: Analysis of MCMC samples: Option 2 (Caveat)
MCMC samples may not conform to a Gaussian distribution
Non-Gaussian sample distribution
Ellipsoid not a good representation of uncertainty for this example
Depth (km)
Longitude

## Slide 39: A note on MCMC: Chain Mixing
The Markov-Chain Represents the distribution when it is “well mixed”
Well mixed means that the chain has reached a steady state.
Think of it as answering the question, “would a subsample give approximately the same answer?”
Not mixed
mixed
Throw away the “burn in” period

## Slide 40: A note on MCMC: Chain Mixing
The Markov-Chain Represents the distribution when it is “well mixed”
Well mixed means that the chain has reached a steady state.
Think of it as answering the question, “would a subsample give approximately the same answer?”
Not mixed
mixed
Not mixed
Throw away the “burn in” period
Inefficient sampling: either need to improve sampling efficiency or run an order of magnitude (or more) iterations

## Slide 41: Some examples of Bayesloc applications: Tomography Data
Relocate global seismicity
Myers et al., 2011 JGR
Tomographic model is smoother and better fits the data
Simmons et al., 2011 (JGR), 2012 (JGR), 2015 (GRL)
Example of image difference
Simmons et al., 2012
Dataset based on iterative relocation
Bayesloc dataset based

## Slide 42: Some examples of Bayesloc applications: Using Priors
Constraint on the January 2016 DPRK nuclear test based on InSAR and finite-element modeling
2006
2013
2016_01
2016_09
2009
Adit for 2006
Adit for 2009
2013
2016
Depths ~1 km ± 1
The events are constrained to specific spots on the mountain
95% coverage ellipse ~0.2 km2
Use the InSAR-based constraint to locate the other DPRK tests
Myers et al., 2018, SRL

## Slide 43
Summary
Bayesian inversion
  Enables probabilistic prior constraints
  Lends itself to stochastic solvers (MCMC)
    High-dimensional spaces
    Non-linear
    Non-parametric
  Caveats
    Better for computationally cheap forward problems
    Theoretically represents the joint probability density when the number of samples is infinite.
      Good approximation when chain is well mixed.

## Slide 44
Resources
Download:
  https://www-gs.llnl.gov/nuclear-threat-reduction/nuclear-explosion-monitoring/bayesloc
  Includes user manual and example data sets
Papers (Myers et al., 2007,2009, 2011, 2018)