## Slide 1
IRIS’s Large N Initiative
Hole, Seismic Instrumentation Technology Workshop, June2012
John Hole, Virginia Tech
Chair of IRIS Large N Working Group
SPATIAL
ALIASING

## Slide 2
Hole, Seismic Instrumentation Technology Workshop, June2012
IRIS’s current instrumentation and field procedures are ~20 years old
this limits the number of instruments per project
most earthquake seismology is badly spatially aliased
currently limited in the science that we can do
new array analysis methods have been developed
directly invert or image using the full wavefield
huge improvement in resolution is possible
but requires data to be not spatially aliased
past decades have seen rapid improvements in technology
improved instruments are possible
improving technology enables new science
IRIS’s Large N Initiative

## Slide 3
Hole, Seismic Instrumentation Technology Workshop, June2012
“Large N” = 1-2 orders of magnitude more instruments per deployment
= unaliased arrays
- much less expensive
- much simpler deploy & retrieve instrument
- much simpler to retrieve data; dirt to desktop solutions
- high quality
- broadest possible range of applications, from 10 m to 10,000 km
transform how we acquire data
IRIS’s Large N Initiative
SPATIAL
ALIASING
resolution
resolution
resolution

## Slide 4
Hole, Seismic Instrumentation Technology Workshop, June2012
Large N Example 1: Russia - USA
M7.7 earthquake
2012-08-13
Sea of Okhotsk, Russia
580 km depth
recorded on
- broadband array
- controlled-source array

## Slide 5
Hole, Seismic Instrumentation Technology Workshop, June2012
EarthScope IDOR (Idaho-Oregon)
450 km long arrays 8 hour drive time 4WD, some hiking
broadband: 85 stations 6 skilled crew 3 months deploy
(29 inline)
controlled-source: 2555 stations 44 beginners + 6 skilled 3 day deploy

## Slide 6
Hole, Seismic Instrumentation Technology Workshop, June2012
EarthScope IDOR (Idaho-Oregon)
P
PcP
0.5-5.0 Hz
60 s
PmS

## Slide 7
Hole, Seismic Instrumentation Technology Workshop, June2012
EarthScope IDOR (Idaho-Oregon)
P
PcP
0.1-1.0 Hz
on 4.5 Hz geophones!
60 s
more traces than pixels!
PmS

## Slide 8
Hole, Seismic Instrumentation Technology Workshop, June2012
EarthScope IDOR (Idaho-Oregon)
P
PcP
1-10 Hz
60 s
PmS

## Slide 9
Hole, Seismic Instrumentation Technology Workshop, June2012
EarthScope IDOR (Idaho-Oregon)
P
PcP
1-10 Hz
60 s
PmS

## Slide 10
Hole, Seismic Instrumentation Technology Workshop, June2012
Large N Example 2: Virginia
M5.8 earthquake
2011-08-23
central Virginia
8 km depth
Washington Monument
National Cathedral
North Anna
nuclear power plant

## Slide 11
Hole, Seismic Instrumentation Technology Workshop, June2012
Aftershock Imaging with Dense Arrays (AIDA) Virginia
blue & red:
traditional aftershock array
42 3-component
some telemetered
~20 people, 3 days
green:
controlled-source sensors
148 1-component
30 3-component
7 people, 1 day

## Slide 12
Hole, Seismic Instrumentation Technology Workshop, June2012
Aftershock Imaging with Dense Arrays (AIDA) Virginia
200 m spacing

## Slide 13
Hole, Seismic Instrumentation Technology Workshop, June2012
Aftershock Imaging with Dense Arrays (AIDA) Virginia
200 m spacing

## Slide 14
Hole, Seismic Instrumentation Technology Workshop, June2012
Aftershock Imaging with Dense Arrays (AIDA) Virginia
Sumatra-Andaman 2004 M9.0 earthquake
Japan HiNET stations @20 km spacing
source back-projection by reverse-time migration
Ishii et al., 2005
300 km
30 s
420 s
resolution ~100 km and ~20 s

## Slide 15
Hole, Seismic Instrumentation Technology Workshop, June2012
Aftershock Imaging with Dense Arrays (AIDA) Virginia
Wang, Hole et al., in prep.
Virginia 2011
M2.9 aftershock
AIDA stations
@200 m spacing
source back-projection
by reverse-time
migration
resolution ~0.5 km
and ~0.05 s
1 km
0 s
0.09 s
0.03 s
0.06 s

## Slide 16
Hole, Seismic Instrumentation Technology Workshop, June2012
Today: 1990’s technology
broadband
~$35k
>100 kg
3-6-hour deployment
long period
high sensitivity
3-component
large memory
GPS
Texan
~$4k
<2 kg
3-minute deployment
for Large N:
combine the best of both
probably some compromises
quantity
quality

## Slide 17
Hole, Seismic Instrumentation Technology Workshop, June2012
Today: 1990’s technology
high-quality waveforms high-quality wavefields
for Large N: combine the best of both
probably some compromises

## Slide 18
Hole, Seismic Instrumentation Technology Workshop, June2012
IRIS 5-year proposal for FY14-18 (starts Oct. 2013)
sustain the core facilities
complete the goals of the EarthScope USArray
facilitate evolving science
create sustainability beyond 2018
proposal approved by NSF, cooperative agreement being negotiated
reduced funding expected
IRIS’s Large N Initiative

## Slide 19
Hole, Seismic Instrumentation Technology Workshop, June2012
IRIS 5-year proposal for FY14-18 (starts Oct. 2013)
sustain the core facilities
complete the goals of the EarthScope USArray
facilitate evolving science
create sustainability beyond 2018
proposal approved by NSF, cooperative agreement being negotiated
reduced funding expected
in the proposal:
IRIS is strongly committed to continue providing existing instrument services
global (to 300 s) through to near-surface (to 1000 Hz)
and
development of Large N
develop, purchase, pilot a Large N deployment
IRIS’s Large N Initiative

## Slide 20
Hole, Seismic Instrumentation Technology Workshop, June2012
plan for implementation
(schedule tentative)
by early 2014:
- develop science objectives, engage stakeholders
(workshop May 2012) (Large N Working Group) (webinars, workshop?)
- compile needs to enable the objectives (no decisions)
- explore technology options and developments (e.g., this meeting)
by summer 2014:
- make technical decisions, compromises (IRIS governance)
- place orders for prototype instruments (~10?)
- design integrated systems for technical support, data support
IRIS’s Large N Initiative

## Slide 21
Hole, Seismic Instrumentation Technology Workshop, June2012
plan for implementation
(schedule tentative)
by summer 2015:
- test prototype instruments
- place place order for prototype array (N = 500-1000?)
- develop integrated systems for technical support, data support
during 2016:
- deploy prototype array in pilot project(s)
by early 2017:
- validate value of Large N system
- fund-raising
by end of 2018:
- place order for multiple large-N systems (MxN = 25,000???)
IRIS’s Large N Initiative

## Slide 22
SPATIAL
ALIASING
Hole, Seismic Instrumentation Technology Workshop, June2012
Goal:
enable unaliased seismic array deployments
completely new science should be enabled
by early 2017:
- acquire Large N datasets
- prove viability of Large N systems
- validate value of Large N datasets
by 2018:
- purchase several Large N systems
IRIS’s Large N Initiative